## Slide 1: Primary Retreat Presentation Slides

## Slide 2: Draft Schedule California WaterFix
2015
2016
2017
USBR|DWR – Environmental Docs
SWRCB – Water Rights | Water Quality
USACE – Permits
USFWS|NOAA|CDFW – Endangered Species Act Authorizations
Final EIR/EIS
ROD/NOD
Water Right New Point of Diversion
Clean Water Act 404
Bio. Assessment/Biological Op. (Sect. 7)
2081(b)
401 Water Quality Certification
2018

## Slide 3
3
Preliminary Subject to Revision
Tunnels
SJ River
Through Delta
CVP Pumps
SWP Pumps
Sacramento
Stockton
Sac River
West Canal
East Canal
SWP Pumps
CVP Pumps
South Delta
Reduces reverse flows in river
Less fish salvage at pumps
North Delta
Modern intake screens allow fish to bypass without salvage
Flexibility to divert excess flood flows & reduce fish impacts during low flow periods
California WaterFix
Proposed Conveyance
X-Channel
Gates Closed
Old & Middle River
- 2,500 cfs limit
South Delta
Reduces reverse flows in river
Less fish diversion at pumps
North Delta
Modern intake screens allow fish to bypass without diversion
Flexibility to divert excess flood flows & reduce fish impacts during low flow periods
Notes: 3
Jan 21 Update
USFWS sent Reclamation a determination implementing Action 2 under the 2008 FWS BiOp and calling for a reduction in OMR to no more negative than -2,500 cfs beginning tomorrow.
OMR as of yesterday was estimated at ~-2,400 cfs so, with increasing San Joaquin River inflows expected to continue through the weekend, the new OMR target may not need to translate into a reduction in current pumping levels.
Subsequent to the FWS determination there was a salvage event at the pumps resulting in the capture of 1 Delta smelt in a 30 minute period, so the expanded value is 4.
Absent a spike in salvage, current operations should be maintained until early next week, when conditions can be reassessed.
Jan 25 Update

## Slide 4
Floodplain restoration
Tidal restoration
Managed wetlands
Prop 1 & 1E funded restoration projects
  Aquatic, Riparian, Upland
  Multi-benefit flood management projects
4
Notes: California EcoRestore is an initiative to help coordinate and advance at least 30,000 acres of critical habitat restoration in the Sacramento – San Joaquin Delta over the next four years. Driven by world-class science and guided by adaptive management, California EcoRestore will aggressively pursue habitat restoration projects with clearly defined goals, measurable objectives, and financial resources to help ensure success.
A broad range of habitat restoration projects will be pursued, including projects to address aquatic, sub-tidal, tidal, riparian, flood plain, and upland ecosystem needs.
California EcoRestore’s initial goal is to advance (i.e. complete or break ground on) 30,000 acres of Delta habitat restoration:
25,000 acres associated with existing mandates for habitat restoration, pursuant to federal biological opinions. These projects will be funded exclusively by the state and federal water contractors that benefit from the State Water Project and the Central Valley Project systems.
5,000 acres of habitat enhancements. Proposition 1 grants to local governments, non-profit organizations, and other entities will support these habitat enhancements throughout the Delta. Funding will come primarily from the Delta Conservancy, the California Department of Fish and Wildlife, and the California Department of Water Resources.
California EcoRestore is unassociated with any habitat restoration that may be required as part of the construction and operation of new Delta water conveyance (California WaterFix).
California EcoRestore Funding
Costs for California EcoRestore are expected to reach at least $300 million in the first four years. Much of these costs will be borne by the state and federal public water agencies currently required to mitigate the ecological impacts of the State Water Project and the Central Valley Project in the Delta.
Funding for habitat enhancements unassociated with mitigation will come primarily from Propositions 1 and 1E, the AB 32 Greenhouse Gas Reduction Fund, and local, federal, and private investment.
More information on California EcoRestore is available through the links below:
EcoRestore Fact Sheet http://resources.ca.gov/ecorestore/

## Slide 5: Back-up Slides by Topic

## Slide 6: Board Retreat – Agenda
Present Video | Metropolitan Water District Video Presentation | 
8:30 – 8:45 PM | Presenter: | General Manager Jeff Kightlinger
 | Objective: | Screen video
1. Call to Order | Opening Remarks from Chairman | 
8:45 – 9:00 AM | Presenter: | Chairman Randy Record
 | Objective: | Welcome and introduce Board Members and others to Day #2 of the retreat. Set objectives for the day.
2. Objectives | General Manager’s Objectives for CA WaterFix Discussion | 
9:00 – 9:15 PM | Presenter: | General Manager Jeff Kightlinger
 | Objectives: | GM welcome. Set purpose and objectives for the discussion of CA WaterFix dialogue. Provide overview of the three topics that will be addressed.
2. Discussion Topic: | Timing and Requirements for Decision-Making | 
9:00 – 10:00 AM | Objective: | Discuss the timing and conditions for decision-making related to CA WaterFix.
 | Outcomes: | Obtain input on the extent of approvals and/or agreements needed before Metropolitan engages in decision-making regarding funding and commitments.
 | Questions: | What stage in the approval process must be reached before addressing decisions regarding next steps in the planning phase (e.g., EIR/EIS approval, ESA permits issued, governance agreement executed, agreement on cost allocation and finance achieved, all of the above)? How should benefits from the CA WaterFix be quantified (e.g., volume received, capacity used)? How should the associated costs be allocated?
3. Communications Break |  | 
10:00 –10:15 AM |  | 

## Slide 7: Board Retreat – Agenda
4. Discussion Topic: | Physical Benefits of California WaterFix | 
10:15 – 12:00 PM | Objective: | Discuss expected benefits and uncertainties associated with CA WaterFix and EcoRestore.
 | Outcomes: | Discussion of Board Member views on the benefits expected from future investments in the Bay-Delta, the uncertainty associated with assurances that they can be achieved, and the affordability of expected outcomes.
 | Questions: | What benefits do the CA WaterFix and EcoRestore offer? What are the uncertainties that threaten the realization of those benefits? What can be done to reduce uncertainties and increase the likelihood of achieving desired benefits? How affordable are the expected benefits compared to other investment opportunities?
5. Lunch Break | 
12:00 –1:00 PM | 
6. Discussion Topic: | CA EcoRestore and Role of Adaptive Mgmt and Science Programs | 
1:00 – 2:30 PM | Objective: | Review and discussion of the regulatory context and proposed approaches to managing uncertainty.
 | Outcomes: | Discussion of Board Member views on future regulatory trends and the potential effectiveness of adaptive management and long-term science program.
 | Questions: | What is needed to respond to lack of regulatory assurances and potential future regulations?
7. Next Steps | Retreat Outcomes and Next Steps | 
2:30 – 3:00 PM | Presenter: | Chairman Randy Record
 | Objective: | Summarize outcomes of the retreat and discuss next steps.
 | Outcomes: | Guidance on next steps following retreat,

## Slide 8: Table of Contents
Topic | Slide Numbers
Primary Slides | 1
Back-Up Slides by Topic | 
CA Water Fix | 8
Finance/Cost Allocation | 14
Increasing Regulatory Trends | 26
Protecting Metropolitan’s Interests (Cost and Schedule) | 37
Supplies/Historic Runoff/Storm Flows | 41
CA WaterFix and IRP | 52
EcoRestore | 64
Emergency Preparedness | 66
Policies and Processes | 72
Water Quality | 77
Delta Wetlands | 82
Other Tunnel/Infrastructure Projects | 85
Staff Reference Only | 90

## Slide 9: CA Water Fix Decisions

## Slide 10: California WaterFix: Securing Water Supplies for California
Enhances supply reliability and Delta ecosystem
Supports Southern California’s local resources
Modernizes the State Water Project and addresses flaws since its creation
Protects billions of dollars of past investments made by Southern California

## Slide 11: California WaterFix Major Permits and Authorizations
Agency | Document | Scope
USBR/DWR | Final EIS/EIR ROD/NOD | Environmental documents and project approval under CEQA and NEPA
USFWS/NMFS | Biological Opinion | Take of threatened or endangered species under Section 7 of ESA
CDFW | Section 2081(b) Permit | Take of threatened or endangered species under CESA
SWRCB | Change in Point of Diversion Permit | Water right permit for new point of diversion for new intakes
SWRCB | Section 401 Certification | Compliance with the state water quality laws and regulations
US Corp | Section 404 Permit | Permit for placement of fill in waters of the U.S. under the CWA
DSC | Consistency Certification | Appeal of Certification of Consistency with the Delta Plan

## Slide 12: Metropolitan Board Policies & Agreements
Policies
  Delta Action Plan Framework Jun 2007
  Delta Conveyance Criteria Sep 2007
  Delta Governance Principles Aug 2008
  Delta Vision Implementation Jan 2009
  Delta-Related Legislation Apr 2009
Funding Agreements
  Execution of Planning Agreement for BDCP Oct 2006
  Execution of BDCP Cost-Sharing Agreement Nov 2006
  Execution of Initial Funding Agreement Dec 2008
  Execution of Amendments to Planning Agmt Dec 2009
  Execution of Amendment (additional funds) July 2010
  Execution of Amendment to MOA Aug 2011

## Slide 13: Metropolitan Board Actions Delta Conveyance Criteria (Sep 2007)
Provide Water Supply Reliability | Consistent with DWR’s State Water Project Reliability Report (2005)
Improve Export Water Quality | Reduce bromide and dissolved organic carbon concentrations
Allow Flexible Pumping Operations in a Dynamic Fishery Environment | Allow the greatest flexibility in meeting water demands by taking water where and when it is least harmful to migrating salmon and in-Delta fish species Reduce inherent conflict between fisheries & water conveyance
Enhance Ecosystem Fishery Habitat Throughout Delta | Provide ability to restore fishery habitat throughout the Delta Minimize disruption to tidal food web processes Provide for fluctuating salinity levels
Reduce Seismic Risks | Provide significant reductions in risks to export water supplies from seismic-induced levee failure and flooding
Reduce Climate Change Risks | Reduce long-term risks from salinity intrusion associated with rising sea levels Intake locations should be able to withstand an estimated 1- to 3-foot sea-level rise in the next 100 years

## Slide 14: State & Federal Project Supplies Annual Average (in 2025)
Chart: SWP-CVP Exports (million AF)
| No Action (with Existing Regs) | No Action (with BDCP Regs) | Earthquake Scenario | BDCP/Cal Water Fix Preferred Alt.
South Delta | 4.7 | 3.5 | 1.5 | 5.3
9,000 cfs Facility
Data based on hydrological period (1922-2003); indicates average annual SWP & CVP water supply exports with climate change in 2025
4.7 maf/yr – Existing Regulations (No Action Alternative) represents no new conveyance and no new/additional restrictions
3.5 maf/yr – BDCP Proposed Regulations without Northern Intake (Existing Conditions High Outflow Scenario); BDCP Chapter 9
1.5 maf/yr – Earthquake scenario BDCP Chapter 9; analyzed by Dr. David Sunding; minimal exports 1.5 to 3 years after earthquake
4.7 – 5.3 maf/yr – NEW BDCP / Cal Water Fix Preferred Alternative (evaluated in Draft EIR/S as Alternative 4A H3-H4)
Notes: 4.9 maf/yr – Current Supplies (2015)
4.7 maf/yr – Existing Regulations (No Action Alternative) represents no new conveyance and no new/additional restrictions
3.5 maf/yr – BDCP Proposed Regulations without Northern Intake represents the Existing Conditions High Outflow (ECHO) scenario without conveyance. Published in Chapter 9 (9.3.4.1.7 -- Practicability of the BDCP Proposed Action Relative to the Existing Conveyance High-Outflow and Low-Outflow Scenarios, pg. 9-45, 9-199, 9-207, 9-216, 9-224, 9-243, 9-250, and elsewhere). Also analyzed by Dr. Sunding, Appendix 9a.
1.5 maf/yr – Earthquake Scenario; Published in BDCP Chapter 9 -- the “mean water supplies following an earthquake in the Existing Conveyance High-Outflow Scenario are 1.0 MAF.” MWD is using a range from 1.0 to 1.5 maf
4.7 – 5.3 maf/yr – NEW BDCP / Cal Water Fix Preferred Alternative (evaluated in Draft EIR/S as Alternative 4A H3-H4 at early long-term 2025)
4.7 – 5.6 maf/yr – PREVIOUS BDCP Preferred Alternative (evaluated in Draft EIR/S as Alternative 4 H1-H4 at early long-term 2025)
MWD Table A = 1,911,500 af/yr. (45.81%)
SWP Table A = 4,172,786 af/yr
SWP/CVP Split: Assume (55% SWP / 45% CVP)
SWP/CVP Average Annual Yield Improvement: Low range (4.7 maf – 3.5 maf = 1.2 maf), High Range (5.3 maf – 3.5 maf = 1.8 maf)
No Action = 3,500,000 af (SWP/CVP); 1,925,000 af SWP; 882,000 af MWD
Cal Water Fix (Lower Yield) = 4,700,000 af (SWP/CVP); 2,585,000 af SWP; 1,184,000 af MWD
Cal Water Fix (Higher Yield) = 5,300,000 af (SWP/CVP); 3,452,000 af SWP; 1,581,000 af MWD

## Slide 15: Finance/Cost Allocation

## Slide 16: California Water Fix Revised Cost Analysis
IMPROVEMENTS | Capital | O&M (Total 50 Years) | TOTAL
Conveyance | $14.99 B | $1.46 B | $16.45 B
Mitigation, Monitoring | $0.56 to $0.82 B | $0.22 B | $0.78 to $1.04 B
TOTAL | $15.55 to $15.81 billion | $1.68 billion | $17.23 to $17.49 billion
Estimated costs from DWR; in undiscounted 2014 dollars with a 36% contingency Metropolitan’s share is approximately 25%
16
Presented to Metropolitan’s Board September 29, 2015
Within $5 per household per month

## Slide 17: California Water Fix Estimated Cost Analysis
Capital Cost | 
Land Acquisition | $0.12 billion
Land Acquisition contingency (20%) | $0.02 billion
Subtotal Land Acquisition | $0.14 billion
Construction | $9.52 billion
Construction Contingency (36%) | $3.41 billion
Subtotal Construction | $12.93 billion
Project, Construction Management and Design | $1.92 billion
TOTAL Capital (with $3.43 billion contingency) | $14.99 billion
Notes: The California WaterFix’s budget consists of two parts: design/construction, and mitigation. The construction budget was developed from a Class III estimate by 5RMK consultants which incorporates the Alternative 4a Conceptual Engineering Report (April 2015). 5RMK created a detailed estimate of construction costs based on the Association for the Advancement of Cost Engineers International (AACEI) standards for 10% design definition, which establishes a Class III estimate. PARO provided the cost estimate for temporary and permanent power. The PM/CM/Eng component of the Project Budget was derived from the anticipated staffing needed for program management, design, and construction management. The California WaterFix budget is in 2014 dollars with a 36% contingency. At this level of project definition the corresponding level of accuracy is +30% to ‐20 %. Estimated costs for mitigation and associated environmental commitments are preliminary and will be revised when permits are granted. The process for estimating these costs are based on a summary and estimate created by ICF, which reflects the change from an HCP/NCCP to a Section 7 consultation. It also considers cost estimates for likely 404 permit requirements, and mitigation measures listed in the EIR/EIS Table 8.A‐61. There are areas of mitigation where the plans are still being finalized and an estimate of cost is very preliminary, including water quality and air quality.
Material Impact
Material changes will be measured against the approved annual budget and schedule. The annual budget and schedule will include an analysis of its proposed impact on the overall project budget and schedule. The intent of the DCE is to share the information developed with DWR and the Authority at quarterly meetings, so that when material impacts are reasonably known the various alternatives and the DCE’s recommendation will be presented to DWR and the Authority as described in Section 3.e.i of the DCE Agreement.

## Slide 18: California Water Fix Estimated Cost Analysis
Mitigation | 
Program Administration | $13 million
Mitigation | $395 million
Monitoring (terrestrial and aquatic) | $134 million
Property tax revenue replacement | $48 million
Contingency (35%) | $206 million
TOTAL (with & without contingency) | $590 – 796 million
Analysis from Cal Water Fix documents
Notes: The California WaterFix’s budget consists of two parts: design/construction, and mitigation. The construction budget was developed from a Class III estimate by 5RMK consultants which incorporates the Alternative 4a Conceptual Engineering Report (April 2015). 5RMK created a detailed estimate of construction costs based on the Association for the Advancement of Cost Engineers International (AACEI) standards for 10% design definition, which establishes a Class III estimate. PARO provided the cost estimate for temporary and permanent power. The PM/CM/Eng component of the Project Budget was derived from the anticipated staffing needed for program management, design, and construction management. The California WaterFix budget is in 2014 dollars with a 36% contingency. At this level of project definition the corresponding level of accuracy is +30% to ‐20 %. Estimated costs for mitigation and associated environmental commitments are preliminary and will be revised when permits are granted. The process for estimating these costs are based on a summary and estimate created by ICF, which reflects the change from an HCP/NCCP to a Section 7 consultation. It also considers cost estimates for likely 404 permit requirements, and mitigation measures listed in the EIR/EIS Table 8.A‐61. There are areas of mitigation where the plans are still being finalized and an estimate of cost is very preliminary, including water quality and air quality.
Material Impact
Material changes will be measured against the approved annual budget and schedule. The annual budget and schedule will include an analysis of its proposed impact on the overall project budget and schedule. The intent of the DCE is to share the information developed with DWR and the Authority at quarterly meetings, so that when material impacts are reasonably known the various alternatives and the DCE’s recommendation will be presented to DWR and the Authority as described in Section 3.e.i of the DCE Agreement.

## Slide 19: Cost Allocation Funding Agencies
Ecosystem Restoration
Conveyance & Mitigation
Federal Government
State of California
CVP/SWP Contractors
Ag
Urban
Exchange
Refuge
Settlement
Ag
Urban
CVP Contractors
SWP Contractors

## Slide 20: Central Valley Project / State Water Project Estimated Costs & Split – Capital, O&M and Mitigation
Based on 2015 assumptions
20
Chart: 
| State Water Project | State / Federal
Cost | 9.603 | 7.857
Share | 0.5519 | 0.45155
State Water Project
$ 9.6 – 10.5 B
(55 - 60% share)
Central Valley Project
$ 7.0 – 7.9 B
(40 – 45% share)
$4.4 – 5.2 billion
$249 – 299 million/yr. (25 – 30% share)
Metropolitan Water District
Notes: MWD Table A = 1,911,500 af/yr. (45.81%)
SWP Table A = 4,172,786 af/yr.
SWP/CVP Split: Assume (55% SWP / 45% CVP)
SWP/CVP Average Annual Yield Improvement: Low range (4.7 maf – 3.5 maf = 1.2 maf),
High Range (5.3 maf – 3.5 maf = 1.8 maf)
No Action = 3,500,000 af (SWP/CVP); 1,925,000 af SWP; 882,000 af MWD
Cal Water Fix (Higher Yield) = 5,300,000 af (SWP/CVP); 2,915,000 af SWP; 1,335,000 af MWD
Improvement (1,335,000 – 882,000 AF) = 453,000 AF
Cal Water Fix (Lower Yield) = 4,700,000 af (SWP/CVP); 2,585,000 af SWP; 1,184,000 af MWD
Improvement (1,184,000 – 882,000 AF) = 302,000 AF
Total Cost = $17.23 to 17.49 billion
CVP (40 – 45%) = $6.89 to 7.87 billion
SWP (55 – 60%) = $9.48 to 10.49 billion
MWD (25 – 30%) = $4.31 to 5.25 billion
MWD Cost/AF
  High Range $5.25 billion, 40 yrs, 6.135%, = $354.88 million per yr / 453,000 AF = $783 + $200 (Power) + $31 (Treatment) = $1,014
  Low Range $4.31 billion, 40 yrs, 6.135%, = $291.34 million per yr / /302,000 = $965 + $200 (Power) + $31 (Treatment) = $1,196
CALSIM (1922-2002) Table A Table ‘A’ Avg. Deliveries Article 21 Avg. Deliveries Table ‘A’ Incremental Article 21 Incremental
  SWP 100% 2,096,700 af/yr. 25,600 af/yr. _______ af/yr. _______ af/yr.
  MWD (100%) 45.8% 960,500 af/yr. 5,400 af/yr. 431,000 af/yr. 67,000 af/yr.
  MWD (110%) 50.4% 960,500 af/yr. 5,400 af/yr. 474,000 af/yr. 74,000 af/yr.
DWR SWP Delivery Reliability Report table
2005 Study: MWD Avg. = 1,418,747 AF/yr (68%); MWD Dry = 430,000 (10 %); Dry year is roughly a 10 percentile.
SWP Table A Delivery (Percent of Demand under then existing condition)
Report Average Minimum Maximum
2005 Study 68% 4% 93%
2007 Study 63% 6% 90%
2009 Study 60% 7% 81%
2011 Study 61% 9% 82%

## Slide 21: State Water Project BDCP Cost Allocation Alternatives
SWP Table ‘A’ Contract Approach
  Participation based on existing Table ‘A’ contract amount
  Payments based on fixed & variable water delivery costs
  Additional provisions for water transfers
Subscribed Capacity Approach
  Participation based on desired capacity amount
  Payments based on fixed & variable water delivery costs
  Additional provisions for water transfers
21
Notes: Main Points
Initial discussions
We still have a ways to go
Allocation Options
Table A – Table A refers to SWP contract entitlement. Payments would be based on contract entitlement. Everyone pays their share but can sell water among contractors in any given year to better manage costs. Allows more mechanisms to move water among contractors; Allows better mgmt between contractors; Note current approach with turn-back pool and permanent transfers
Variable BDCP Participation­Out-In/Op-Out – Some contractors have put that forward; its on the table;
Follow the Water Approach -- Pay based on delivered water, would need to turn-up costs at end of year
Two Primary Components
  Subscription to Define Level of Participation in BDCP
  Provide Additional Options for Managing Water Supplies and Cost
Subscription process identifies actual participation
  Contractors request desired capacity amount
  Actual purchase adjusted based on total requests

## Slide 22
Labor costs include salary, leave and non-leave benefits
Other include charges for materials & supplies, trainings & seminars, conferences & meetings, and reprographics
MWD Expenditures on BDCP
Total (Jul 2005 – Sep 2015)
BDCP – Internal MWD Total Costs (~10 yrs.)
  Labor & Benefits (1) $ 20.91M
  Professional Services $ 4.15M
  Travel $ 1.03M
  Other (2) $ 0.14M
    Subtotal $ 26.23M
    Administrative Overhead $ 7.97M
    Total $ 34.20M
BDCP – Planning Cost by DWR
  BDCP/DHCCP $ 63M
As reported to Board on October 27, 2015
Notes: Labor
Based on staff estimates prior to 2011; Actual time from 2011 to present
Professional Services
Firms hired by MWD include – Dalldorf, Spezia, Beacon Economics, MWH, CDM, Cardno-Entrix, HNTB, AECOM, CH2MHill, Black & Veatch, URS, Geosyntech, ARUP, Anchor, Southern Cal Water Committee; Jacobs, Breakdown based on BDCP specific task orders through July 2015. Beginning FY 2015-16, all costs are tracked under PN 601118 although there are still some charges to old project numbers that were captured due to timing of invoice processing and adjustments for charges that were not previously reported.
Travel
Based on staff estimates prior to 2011; From 2011-2012, staff were charging to travel codes specific to BDCP; Starting in 2012, some staff began charging to a general Bay Delta code (PM07 – Travel, Incidentals, training, conferences, supplies, etc.), while others continued to charge to specific BDCP travel codes. Beginning in March 2015, staff started charging to specific projects to ensure that costs are properly reported.
Other
Others include charges for materials & supplies, trainings, seminars, conferences/meetings, & reprographics
Legal
Legal has a separate labor charge system; BDCP labor charges are not fully separated from other tasks; Labor calculated based on staff estimates of time spent on BDCP. Beginning in FY15-16, Legal has been reporting actual labor that are project specific.
FY2015-16 Cost Tracking
Tracking of BDCP expenditures have been consolidated under the same PN601118 beginning July 1, 2015. There are still some charges that were captured from the old project numbers mainly due to timing of data processing and reporting. These charges have since diminished and will hopefully end by the 2nd quarter for the fiscal year.

## Slide 23
Bay Delta Conservation Plan
Planning Agreement Payments (thru March 2016)
Metropolitan Total Share - $63 million
Prior to these funding agreements, an additional $13.5 million was expended under the November 2006 BDCP Cooperative Cost-Share Agreement for startup costs related to development and review of the BDCP and consulting resources necessary to prepare the BDCP.
Funding Agreements | Total Project (in millions) |  | 
 | Budget | Incurred | Remaining
Dec 2008 – DHCCP Funding Agreement | $139.6 | $139.6 | $0
Jul 2010 – Supplemental Funding Agreement | $100.0 | $100.0 | $0
USBR Federal Funding Agreement | $ 5.7 | $ 5.3 | $.4
TOTAL | $245.3 | $244.9 | $.4

## Slide 24: California Water Fix 2% Impact on Metropolitan Water Rates
Rate impact for customers that are 50% reliant on MWD
  1.6% to 2% per year for 10 years
Overall rate increase (with CA WaterFix)
  ~ 3% to 5% per year
24
  * Based on a 20 hundred cubic feet average water bill

## Slide 25
Rate Impact of Water Fix*
  Annual increase of 1.6 to 2% per year for 10 years.
Overall Rate Increase
  When accounting for the cost of the Water Fix, MWD’s overall rates are expected to increase 3% to 5% per year.
Sales | $/AF
1.75 million AF | $142 to $171
2.00 million AF | $125 to $150
  * Based on a Draft DWR Estimate
California Water Fix 2% Impact on Metropolitan Water Rates

## Slide 26: California Water Fix Protecting Metropolitan’s Supplies
 | Lower Yield | Higher Yield
MWD’s SWP Improvement | 302,000 af | 453,000 af
Water supply based on DWR CALSIM modeling of average Table A & incremental Cal Water Fix allocations
Notes: MWD Table A = 1,911,500 af/yr. (45.81%)
SWP Table A = 4,172,786 af/yr
SWP/CVP Split: Assume (55% SWP / 45% CVP)
SWP/CVP Average Annual Yield Improvement: Low range (4.7 maf – 3.5 maf = 1.2 maf),
High Range (5.3 maf – 3.5 maf = 1.8 maf)
No Action = 3,500,000 af (SWP/CVP); 1,925,000 af SWP; 882,000 af MWD
Cal Water Fix (Higher Yield) = 5,300,000 af (SWP/CVP); 2,915,000 af SWP; 1,335,000 af MWD
Improvement (1,335,000 – 882,000 AF) = 453,000 AF
Cal Water Fix (Lower Yield) = 4,700,000 af (SWP/CVP); 2,585,000 af SWP; 1,184,000 af MWD
Improvement (1,184,000 – 882,000 AF) = 302,000 AF
Total Cost = $17.23 to 17.49 billion
CVP (40 – 45%) = $6.89 to 7.87 billion
SWP (55 – 60%) = $9.48 to 10.49 billion
MWD (25 – 30%) = $4.31 to 5.25 billion
MWD Cost/AF
  High Range $5.25 billion, 40 yrs, 6.135%, = $354.88 million per yr / 453,000 AF = $783 + $200 (Power) + $31 (Treatment) = $1,014
  Low Range $4.31 billion, 40 yrs, 6.135%, = $291.34 million per yr / /302,000 = $965 + $200 (Power) + $31 (Treatment) = $1,196
CALSIM (1922-2002) Table A Table ‘A’ Avg. Deliveries Article 21 Avg. Deliveries Table ‘A’ Incremental Article 21 Incremental
  SWP 100% 2,096,700 af/yr. 25,600 af/yr. _______ af/yr. _______ af/yr.
  MWD (100%) 45.8% 960,500 af/yr. 5,400 af/yr. 431,000 af/yr. 67,000 af/yr.
  MWD (110%) 50.4% 960,500 af/yr. 5,400 af/yr. 474,000 af/yr. 74,000 af/yr.
DWR SWP Delivery Reliability Report table
2005 Study: MWD Avg. = 1,418,747 AF/yr (68%); MWD Dry = 430,000 (10 %); Dry year is roughly a 10 percentile.
SWP Table A Delivery (Percent of Demand under then existing condition)
Report Average Minimum Maximum
2005 Study 68% 4% 93%
2007 Study 63% 6% 90%
2009 Study 60% 7% 81%
2011 Study 61% 9% 82%
2013 Study 62% 12% 97%
_____________________________________________ From: Chan,Grace L Sent: Wednesday, April 30, 2014 5:16 PM To: Upadhyay,Devendra N Subject: SWP minimum delivery from reliability report
Deven, The table below shows the delivery from DWR SWP Delivery Reliability Reports over the years.
The 2010 IRP was based on the draft 2011 report, so the current condition would be a minimum delivery of 9%. However, when we revert to 2005 reliability profile after Delta improvement the minimum was lowered. The reasoning is that with higher annual delivery, you may have a lower starting reservoir level when you get into drought and result with a lower minimum delivery.
DWR stated that the 2013 and 2011 study are actually comparable. DWR’s explanation of higher delivery numbers because all contractors have requested their maximum Table A amount and higher demands mean higher maximum delivery. However, the minimum delivery also increased and DWR attributed that to model refinements.

## Slide 27: Increasing Regulatory Trends

## Slide 28
Chart: Avg. SWP-CVP Export Capacity (MAF)
| 1980's | 1991 NMFS BioOp | 1992 CVPIA | 1994 Accord | 2000 Trinity River | 2006 San Joaquin River | 2008-09 Smelt/ Salmon BioOp | Future
SWP-CVP Exports | 8 | 7.9 | 6.7 | 6.2 | 5.6 | 5.4 | 4.7
9,000 cfs Facility
BDCP Enhanced Reliability
BDCP Replacement Supplies
SWP/CVP Export Capacity Restrictions Due to Environmental Regulations
State & Federal Project Supplies
History of Regulatory Restrictions
?

## Slide 29: Sacramento/San Joaquin Bay-Delta
Sacramento River
San Joaquin River
Sacramento River/ West Delta
Sacramento
Stockton
SWP Pumps
CVP Pumps

## Slide 30: Delta Fisheries Endangered Species Act Listings
Chinook Salmon
1989 – Winter-Run: Endangered (CESA)
1990 – Winter-Run: Endangered (FESA)
1999 – Spring-Run: Threatened (CESA/FESA)
Green Sturgeon
2006 – Threatened (FESA)
No CESA listing
Steelhead
1998 – Threatened (FESA)
No CESA listing
Sacramento Splittail
1999 – Threatened (FESA)
2003 – FESA listing removed
No CESA listing
Longfin smelt
2007 – Threatened (CESA)
Delta smelt
1993 – Threatened (CESA/FESA)
Notes: There are several ESA species & other species of concern…….
This slide shows the current listing status …..
Note that the Longfin smelt has a 2007 petition under consideration….
This demonstrates that the Delta fishery risks continue well into the future & that risk equates to water supply risks….
Species Fed ESA Cal ESA
Delta Smelt 1993 (T) 1993 (T)
Steelhead 1998 (T) N
Sacramento Splittail* N N
Green Sturgeon 2006 (T) N
Chinook Salmon (winter run) 1990 (E) 1989 (E)
Chinook Salmon (spring run) 1999 (T) 1999 (T)
Longfin Smelt 2007 (P) 2007 (P)
*Splittail was Federally listed in 1999 & removed from the list in 2003….
T=Threatened, E=Endangered, N=Not Listed, P=Petition under consideration….

## Slide 31
31
Preliminary Subject to Revision
Tunnels
SJ River
Through Delta
CVP Pumps
SWP Pumps
Sacramento
Stockton
Sac River
West Canal
East Canal
SWP Pumps
CVP Pumps
South Delta
Reduces reverse flows in river
Less fish salvage at pumps
North Delta
Modern intake screens allow fish to bypass without salvage
Flexibility to divert excess flood flows & reduce fish impacts during low flow periods
Improving Ecosystems through Adaptive Management
X-Channel
Gates Closed
Old & Middle River
- 2,500 cfs limit
Ecosystem Restoration
Turbidity Management
Water Quality Improvements
Notes: 31
Jan 21 Update
USFWS sent Reclamation a determination implementing Action 2 under the 2008 FWS BiOp and calling for a reduction in OMR to no more negative than -2,500 cfs beginning tomorrow.
OMR as of yesterday was estimated at ~-2,400 cfs so, with increasing San Joaquin River inflows expected to continue through the weekend, the new OMR target may not need to translate into a reduction in current pumping levels.
Subsequent to the FWS determination there was a salvage event at the pumps resulting in the capture of 1 Delta smelt in a 30 minute period, so the expanded value is 4.
Absent a spike in salvage, current operations should be maintained until early next week, when conditions can be reassessed.
Jan 25 Update

## Slide 32
Impacts of Regulation
On California’s Water Supply
Year | State/Federal Project Impacts
2008 | 655,000
2009 | 336,000
2010 | 1,080,000
2011 | 611,000
2012 | 634,000
2013 | 1,027,000
2014 | 65,000
2015 | 250,000
2016 * | 503,000
TOTAL | 5.2 million AF
* 2016 data thru March 3
32
Notes: Based on impacts to both SWP and CVP over the 9 year implementation of the biological opinions
2016 data
  Thru March 3 – 503,000 AF
  Thru March 17 – 560,000 AF
9 years of regulations under current BioOps
5.2 million acre-feet total or 580,000 AF/year
Replacement supply:
  580,000 AF/year average losses or enough for 4.6 million residents /year or 1.1 million homes/year
  12 desalination plants (at 50,000 AF/yr.)
  Enough water to produce crops on 145,000 acres (4 acre-ft per acre)
In 2013
“Last years 800,000 acre-feet of water went to waste based on the science of four buckets of minnows … enough water to produce crops on 200,000 acres or 10 million tons of tomatoes; 200 million boxes of lettuce; 20 million tons of grapes.” -- Harry Cline, Western Farm Press, Feb 2013

## Slide 33
Bay Delta Conservation Plan
Collaborative Science & Adaptive Management
Ongoing Collaborative Science
  Two-tiered collaborate policy & technical team
  Conducts joint research on key Delta fishery issues
  Includes
    United States Fish and Wildlife Service
    National Marine Fisheries Service
    California Department of Fish and Wildlife
    United States Bureau of Reclamation
    California Department of Water Resources
    Environmental interests (NRDC, TNC, PCFFA and Water4Fish)
    Non-Governmental Organizations
    State and Federal water contractors
Notes: General Background
The CSAMP was launched following a decision by the United States District Court for the Eastern
District of California on April 9, 2013 entitled “Memorandum Decision and Order regarding
Motion to Extend Remand Schedule” (“Court Order”), issued in response to a motion to extend
the court3ordered remand schedule for completing revisions to salmon (NMFS 2009) and Delta
Smelt (FWS 2008) Biological Opinions (“BiOps”).
CSAMP Policy Group
Jim Beck…….……………………………………….…………... Kern County Water Agency
Thomas Birmingham……………………………………….. Westlands Water District
Charlton “Chuck” Bonham….……………………….….. CA Department of Fish and Wildlife
Mark Cowin………………….…………………………………. CA Department of Water Resources
Zeke Grader…………………………………………………….. Golden Gate Salmon Association
Ren Lohoefener………………………………………………. U.S. Fish and Wildlife Service
Jeff Kightlinger..………………………………………………. Metropolitan Water District of Southern California
David Murillo…………………………………………………… U.S. Bureau of Reclamation
Bill Phillimore………………………………………………….. Coalition for a Sustainable Delta
Dick Pool…………...……………………………………………. Water4Fish
Kate Poole……….................................................... Natural Resources Defense Council
William Stelle....................................................... National Marine Fisheries Service
Jay Ziegler…..…………............................................. The Nature Conservancy
Collaborative Adaptive Management Team (CAMT)
Gary Bobker………………………………………………….... The Bay Institute
Frances Brewster…………………………………………….. Santa Clara Valley Water District
Mike Chotkowski…………………………………………….. U.S. Fish and Wildlife Service
Valerie Connor, Co-Chair…………………………………. State and Federal Contractors Water Agency
Sue Fry…………………………………………………………….. U.S. Bureau of Reclamation
Lauren Hastings………………………………………………. Delta Science Program
Steve Lindley…………………………………………………… National Marine Fisheries Service
Laura King Moon.................................................. CA Department of Water Resources
Anke Mueller-Solger............................................ Interagency Ecological Program
Maria Rea............................................................. National Marine Fisheries Service
Carl Wilcox........................................................... CA Department of Fish and Wildlife
Leo Winternitz, Co-Chair...................................... The Nature Conservancy

## Slide 34
Bay Delta Conservation Plan
Collaborative Science & Adaptive Management
Adaptive Management & Monitoring Plan
  Mechanism to review and appropriately adjust existing and new operating requirements based on new scientific information and monitoring
  Addresses gaps in knowledge
  Demonstrate project avoids jeopardy to listed species
Notes: General Background
The CSAMP was launched following a decision by the United States District Court for the Eastern
District of California on April 9, 2013 entitled “Memorandum Decision and Order regarding
Motion to Extend Remand Schedule” (“Court Order”), issued in response to a motion to extend
the court3ordered remand schedule for completing revisions to salmon (NMFS 2009) and Delta
Smelt (FWS 2008) Biological Opinions (“BiOps”).
CSAMP Policy Group
Jim Beck…….……………………………………….…………... Kern County Water Agency
Thomas Birmingham……………………………………….. Westlands Water District
Charlton “Chuck” Bonham….……………………….….. CA Department of Fish and Wildlife
Mark Cowin………………….…………………………………. CA Department of Water Resources
Zeke Grader…………………………………………………….. Golden Gate Salmon Association
Ren Lohoefener………………………………………………. U.S. Fish and Wildlife Service
Jeff Kightlinger..………………………………………………. Metropolitan Water District of Southern California
David Murillo…………………………………………………… U.S. Bureau of Reclamation
Bill Phillimore………………………………………………….. Coalition for a Sustainable Delta
Dick Pool…………...……………………………………………. Water4Fish
Kate Poole……….................................................... Natural Resources Defense Council
William Stelle....................................................... National Marine Fisheries Service
Jay Ziegler…..…………............................................. The Nature Conservancy
Collaborative Adaptive Management Team (CAMT)
Gary Bobker………………………………………………….... The Bay Institute
Frances Brewster…………………………………………….. Santa Clara Valley Water District
Mike Chotkowski…………………………………………….. U.S. Fish and Wildlife Service
Valerie Connor, Co-Chair…………………………………. State and Federal Contractors Water Agency
Sue Fry…………………………………………………………….. U.S. Bureau of Reclamation
Lauren Hastings………………………………………………. Delta Science Program
Steve Lindley…………………………………………………… National Marine Fisheries Service
Laura King Moon.................................................. CA Department of Water Resources
Anke Mueller-Solger............................................ Interagency Ecological Program
Maria Rea............................................................. National Marine Fisheries Service
Carl Wilcox........................................................... CA Department of Fish and Wildlife
Leo Winternitz, Co-Chair...................................... The Nature Conservancy

## Slide 35: Adaptive Management Conceptual Process
Tech
Teams
Collaborative
Science
Proposed Management Actions Based on Science
Agencies and Contractors
Action Agencies
DWR, USBR
USFWS
NMFS
CDFW
Funding Science Needs
Science
Proposals/ Recommendations
Regulatory Response
Reinitiate Consultation
Recommendations
Future
Direction
Results

## Slide 36: State Water Resources Control Board Water Right Change Petition Process
Application Filed by DWR/Reclamation & Accepted by SWRCB August 26, 2015
SWRCB Water Rights Decision
Coupled with Separate 401 Water Quality Certification
Public Notice Oct 30, 2015
Protests Filed
Jan 5, 2016
SWRCB Hearing-
Part A
TBD - Originally
Apr 7, 2016
SWRCB Hearing-Part B
Post FEIR/EIS Completion
Notes: How long does it take to get a water right permit?
It depends on the project. SWRCB must comply with Water Code requirements and with CEQA. The time it takes to obtain a permit depends on:
  The effects that the project could have on other water rights;
  The effects the project could have on the environment, including aquatic species, particularly endangered species;
  Whether anyone protests against issuing the permit applicant a water right permit;
  Whether there are other applicants competing for the same water supply;
  SWRCB staffing resources.
The SWRCB has in excess of 500 pending water right applications. On average, if the permit applicant can provide all the necessary information, it may take three to four years to obtain a permit. If others protest the project or the project has the capacity to harm threatened or endangered species, it could take longer to get a permit.
What will each SWRCB hearing consider?
PART A of Hearing would focus on the potential effects of the Petition on agricultural, municipal and industrial uses of water and associated legal users of water and conditions that should be placed on any approval of the Petition to protect those uses.
PART B of Hearing would focus on the potential effects of the Petition on fish and wildlife and recreational uses and conditions that should be placed on any approval of the Petition to protect those uses, including consideration of appropriate Delta flow criteria for the California WaterFix Project.

## Slide 37: Adaptive Management A Long-Term Science Program
Management actions based on collaborative science
Other Delta water agencies are taking similar approaches
  Alternative intake locations
  Adaptive management
  Better science
Metropolitan representation on both technical and policy teams to protect Metropolitan’s interests
Metropolitan has a recognized science program that contributes to decisions being made

## Slide 38: Cost and Schedule Management

## Slide 39: Design & Construction Enterprise Overview
Design & Construction Enterprise
(Special Purpose Enterprise)
Program Director | Staff | Consultants
Program Advisory Group
(Tech Experts)
Program Management
Conveyance Project Coordination Agency
(Public Joint Powers Authority)
Department of Water Resources
(DWR Director)
The Director of the Department of Water Resources has the final decision making authority on all aspects of the design, construction and implementation of the Conveyance Project
Notes: Conveyance Project Coordination Agency
Consists of water agencies that contract for water supplies from the SWP & CVP
Makes recommendations to DWR Director
Program Advisory Group
Will advise Program Director on technical issues
It will consist of DWR and PWA technical staff
Ad hoc in nature
Reviews recommendations of Project Management Board; will meet and confer if inconsistent with the project purposes or DWR’s mandatory legal duty
Design & Construction Enterprise
Special Purpose Enterprise within DWR dedicated to the design and construction of the Conveyance Project
Program Director
Authority over staffing decisions
Retained to manage design and construction
Selected by DWR Director with the concurrence of JPA
Reports to Project Management Board

## Slide 40: Design & Construction Enterprise
Funding
Management
DCE
Conveyance Project Coordination Agency
DWR
San Luis & Delta Mendota Water Authority
SWP
Contractors
DCE
DWR
San Luis & Delta Mendota Water Authority
SWP Contractors
SWP
JPA
Design & Construction Enterprise
Special Purpose Enterprise within DWR dedicated to the design and construction of the conveyance Project
40
Notes: Conveyance Project Coordination Agency
Consists of water agencies that contract for water supplies from the SWP & CVP
Makes recommendations to DWR Director
Program Advisory Group
Will advise Program Director on technical issues
It will consist of DWR and PWA technical staff
Ad hoc in nature
Reviews recommendations of Project Management Board; will meet and confer if inconsistent with the project purposes or DWR’s mandatory legal duty
Design & Construction Enterprise
Special Purpose Enterprise within DWR dedicated to the design and construction of the Conveyance Project
Program Director
Authority over staffing decisions
Retained to manage design and construction
Selected by DWR Director with the concurrence of JPA
Reports to Project Management Board

## Slide 41: Cost and Schedule Control
Transparency
Accountability
Real-time reporting & updates
Records management
Oversight & independent audits

## Slide 42: Supplies/Historic Runoff/ Storm Flows

## Slide 43: Excess Storm Flow Analysis Sacramento Watershed Annual Runoff
Chart: Runoff (million acre-ft.)
1983 38 million af
Average 18 million af
Sacramento Four Rivers Runoff (1906-2014 – Sacramento, Feather, Yuba, American)
Notes: 2014 Water Year Forecast as of March 1, 2014
Sac River Unimpaired Runoff
Mar 1 -- 5.1 million af (90 percentile) 5.9 million af (75 percentile) 6.6 million af (50 percentile)
Sacramento River Runoff is the sum of unimpaired flow in million acre-feet at:
Sacramento River above Bend Bridge
Feather River at Oroville (aka inflow to Lake Oroville)
Yuba River near Smartville
American River below Folsom Lake
Also known as the "Sacramento River Index", this index was previously used to determine year type classifications under SWRCB Decision 1485. Also previously referred to as the "4 River Index" or "4 Basin Index".
Water Year Runoff through end of last month:
2014 (current year) = 2.5 million AF, 30% of average
2013 (last year) = 6.8 million AF, 84% of average
Previous Water Year Total Runoff:
2013 – 11.9 million AF (65% of average)
1977 (Min) – 5.1 million AF (28% of average)
1983 (Max) – 37.7 million AF (206% of average)
1961-2010 average – 18.3 million af/yr.
1906-2013 average – 17.9 million af/yr.
2004-2013 average – 16.5 million af/yr.
Water-Year Type % of 82-yr Record
Wet 32%
Above-normal 15%
Below-normal 17%
Dry 22%
Critical 15%

## Slide 44: Excess Storm Flow Analysis Sacramento Watershed Annual Runoff
Chart: Runoff (million acre-ft.)
1983 38 million af
1977 5 million af
Sacramento Four Rivers Runoff (1906-2014 – Sacramento, Feather, Yuba, American)
Notes: 2014 Water Year Forecast as of March 1, 2014
Sac River Unimpaired Runoff
Mar 1 -- 5.1 million af (90 percentile) 5.9 million af (75 percentile) 6.6 million af (50 percentile)
Sacramento River Runoff is the sum of unimpaired flow in million acre-feet at:
Sacramento River above Bend Bridge
Feather River at Oroville (aka inflow to Lake Oroville)
Yuba River near Smartville
American River below Folsom Lake
Also known as the "Sacramento River Index", this index was previously used to determine year type classifications under SWRCB Decision 1485. Also previously referred to as the "4 River Index" or "4 Basin Index".
Water Year Runoff through end of last month:
2014 (current year) = 2.5 million AF, 30% of average
2013 (last year) = 6.8 million AF, 84% of average
Previous Water Year Total Runoff:
2013 – 11.9 million AF (65% of average)
1977 (Min) – 5.1 million AF (28% of average)
1983 (Max) – 37.7 million AF (206% of average)
1961-2010 average – 18.3 million af/yr.
1906-2013 average – 17.9 million af/yr.
2004-2013 average – 16.5 million af/yr.
Water-Year Type % of 82-yr Record
Wet 32%
Above-normal 15%
Below-normal 17%
Dry 22%
Critical 15%

## Slide 45: Sacramento Four Rivers Runoff (1906-2015 – Sacramento, Feather, Yuba, American)
Chart: Runoff (million acre-ft.)
| 1906 | 1907 | 1908 | 1909 | 1910 | 1911 | 1912 | 1913 | 1914 | 1915 | 1916 | 1917 | 1918 | 1919 | 1920 | 1921 | 1922 | 1923 | 1924 | 1925 | 1926 | 1927 | 1928 | 1929 | 1930 | 1931 | 1932 | 1933 | 1934 | 1935 | 1936 | 1937 | 1938 | 1939 | 1940 | 1941 | 1942 | 1943 | 1944 | 1945 | 1946 | 1947 | 1948 | 1949 | 1950 | 1951 | 1952 | 1953 | 1954 | 1955 | 1956 | 1957 | 1958 | 1959 | 1960 | 1961 | 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Wet | 26.71 | 33.7 | 30.68 | 20.12 | 26.38 | 27.81 | 23.86 | 24.14 | 23.83 | 31.83 | 27.08 | 25.24 | 21.13 | 28.6 | 20.09 | 29.89 | 29.71 | 22.99 | 25.64 | 24.06 | 26.98 | 24.06 | 22.57 | 32.5 | 19.23 | 33.53 | 37.65 | 22.35 | 25.72 | 34.45 | 22.25 | 25.4 | 31.36 | 21.19 | 32.09 | 25.21
Above Normal | 17.26 | 23.8 | 17.98 | 16.76 | 22.43 | 22.95 | 17.43 | 14.89 | 20.05 | 22.33 | 22.33 | 22.17 | 18.9 | 19.18 | 18.55
Below Normal | 14.77 | 11.41 | 15.66 | 13.21 | 16.59 | 17.35 | 13.33 | 15.06 | 17.62 | 15.75 | 14.44 | 12.05 | 15.11 | 13.64 | 13.64 | 13.43 | 12.41 | 16.04 | 16.01 | 11.84
Dry | 12.85 | 10.99 | 15.99 | 11.76 | 13.52 | 13.12 | 8.18 | 10.43 | 10.39 | 11.97 | 10.98 | 13.06 | 11.97 | 10.92 | 11.1 | 11.04 | 9.2 | 14.8 | 9.81 | 14.6 | 10.28 | 13.02 | 12.19
Critical | 9.2 | 5.74 | 8.4 | 6.1 | 8.94 | 8.64 | 8.22 | 5.12 | 9.19 | 9.23 | 8.45 | 8.92 | 7.77 | 10.28 | 7.47 | 9.5
Avg. Runoff (1906-2015) – 18 million acre-feet/year (2006-2015) – 15 million acre-feet/year
Notes: Comparison (MAF) Avg Min Max
1906 - 2015 17.8 5.1 37.7
1922 - 2003 17.6 5.1 37.7
2003 - 2015 15.7 7.5 32.1
1922 - 2015 17.3 5.1 37.7
2006 - 2015 14.8 7.5 32.1

## Slide 46: Sacramento Four Rivers Runoff (1906-2015 – Sacramento, Feather, Yuba, American)
Chart: Runoff (million acre-ft.)
| 1906 | 1907 | 1908 | 1909 | 1910 | 1911 | 1912 | 1913 | 1914 | 1915 | 1916 | 1917 | 1918 | 1919 | 1920 | 1921 | 1922 | 1923 | 1924 | 1925 | 1926 | 1927 | 1928 | 1929 | 1930 | 1931 | 1932 | 1933 | 1934 | 1935 | 1936 | 1937 | 1938 | 1939 | 1940 | 1941 | 1942 | 1943 | 1944 | 1945 | 1946 | 1947 | 1948 | 1949 | 1950 | 1951 | 1952 | 1953 | 1954 | 1955 | 1956 | 1957 | 1958 | 1959 | 1960 | 1961 | 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Wet | 26.71 | 33.7 | 30.68 | 20.12 | 26.38 | 27.81 | 23.86 | 24.14 | 23.83 | 31.83 | 27.08 | 25.24 | 21.13 | 28.6 | 20.09 | 29.89 | 29.71 | 22.99 | 25.64 | 24.06 | 26.98 | 24.06 | 22.57 | 32.5 | 19.23 | 33.53 | 37.65 | 22.35 | 25.72 | 34.45 | 22.25 | 25.4 | 31.36 | 21.19 | 32.09 | 25.21
Above Normal | 17.26 | 23.8 | 17.98 | 16.76 | 22.43 | 22.95 | 17.43 | 14.89 | 20.05 | 22.33 | 22.33 | 22.17 | 18.9 | 19.18 | 18.55
Below Normal | 14.77 | 11.41 | 15.66 | 13.21 | 16.59 | 17.35 | 13.33 | 15.06 | 17.62 | 15.75 | 14.44 | 12.05 | 15.11 | 13.64 | 13.64 | 13.43 | 12.41 | 16.04 | 16.01 | 11.84
Dry | 12.85 | 10.99 | 15.99 | 11.76 | 13.52 | 13.12 | 8.18 | 10.43 | 10.39 | 11.97 | 10.98 | 13.06 | 11.97 | 10.92 | 11.1 | 11.04 | 9.2 | 14.8 | 9.81 | 14.6 | 10.28 | 13.02 | 12.19
Critical | 9.2 | 5.74 | 8.4 | 6.1 | 8.94 | 8.64 | 8.22 | 5.12 | 9.19 | 9.23 | 8.45 | 8.92 | 7.77 | 10.28 | 7.47 | 9.5
 | Period | Runoff (Avg.)
Full Record | 1906 - 2015 | 18 million acre-ft.
Last 10 yrs | 2006 - 2015 | 15 million acre-ft.
CalSim II Model | 1922 - 2003 | 18 million acre-ft.
CalSim III Model | 1922 - 2015 | 16 million acre-ft.
Updating
Notes: Comparison (MAF) Avg Min Max
1906 - 2015 17.8 5.1 37.7
1922 - 2003 17.6 5.1 37.7
2003 - 2015 15.7 7.5 32.1
1922 - 2015 17.3 5.1 37.7
2006 - 2015 14.8 7.5 32.1

## Slide 47: Sacramento Four Rivers Runoff (1906-2015 – Sacramento, Feather, Yuba, American)
Chart: Runoff (million acre-ft.)
| 1977 | 1924 | 1931 | 2014 | 1994 | 1939 | 1976 | 1929 | 1991 | 1934 | 1992 | 1933 | 1988 | 1920 | 1987 | 1990 | 2015 | 2001 | 2007 | 2008 | 1947 | 1944 | 1964 | 1955 | 1918 | 1985 | 1981 | 1912 | 1926 | 2012 | 1949 | 1961 | 1959 | 2013 | 1979 | 1913 | 2009 | 1960 | 1932 | 1923 | 1937 | 1972 | 1930 | 1966 | 1968 | 1950 | 2002 | 1908 | 1989 | 1957 | 1945 | 1962 | 1919 | 1948 | 1925 | 2010 | 2004 | 1935 | 1928 | 1917 | 1936 | 1954 | 1946 | 1922 | 2005 | 2000 | 2003 | 1975 | 1973 | 1953 | 1910 | 1943 | 1993 | 1999 | 1996 | 1978 | 1980 | 1984 | 1940 | 1971 | 1951 | 1963 | 1921 | 1927 | 1915 | 1967 | 1970 | 1916 | 2011 | 1942 | 1997 | 1965 | 1986 | 1911 | 1906 | 1969 | 1941 | 1914 | 1952 | 1958 | 1956 | 1909 | 1998 | 1938 | 2006 | 1974 | 1982 | 1907 | 1995 | 1983
Wet | 19.23 | 20.09 | 20.12 | 21.13 | 21.19 | 22.25 | 22.35 | 22.57 | 22.99 | 23.83 | 23.86 | 24.06 | 24.06 | 24.14 | 25.21 | 25.24 | 25.4 | 25.64 | 25.72 | 26.38 | 26.71 | 26.98 | 27.08 | 27.81 | 28.6 | 29.71 | 29.89 | 30.68 | 31.36 | 31.83 | 32.09 | 32.5 | 33.53 | 33.7 | 34.45 | 37.65
Above Normal | 14.89 | 16.76 | 17.26 | 17.43 | 17.98 | 18.55 | 18.9 | 19.18 | 20.05 | 22.17 | 22.33 | 22.33 | 22.43 | 22.95 | 23.8
Below Normal | 11.41 | 11.84 | 12.05 | 12.41 | 13.21 | 13.33 | 13.43 | 13.64 | 13.64 | 14.44 | 14.77 | 15.06 | 15.11 | 15.66 | 15.75 | 16.01 | 16.04 | 16.59 | 17.35 | 17.62
Dry | 8.18 | 9.2 | 9.81 | 10.28 | 10.39 | 10.43 | 10.92 | 10.98 | 10.99 | 11.04 | 11.1 | 11.76 | 11.97 | 11.97 | 12.19 | 12.85 | 13.02 | 13.06 | 13.12 | 13.52 | 14.6 | 14.8 | 15.99
Critical | 5.12 | 5.74 | 6.1 | 7.47 | 7.77 | 8.22 | 8.4 | 8.45 | 8.64 | 8.92 | 8.94 | 9.19 | 9.2 | 9.23 | 9.5 | 10.28
Avg. Runoff (1906-2015) – 18 million acre-feet/year (2006-2015) – 15 million acre-feet/year
Notes: Comparison (MAF) Avg Min Max
1906 - 2015 17.8 5.1 37.7
1922 - 2003 17.6 5.1 37.7
2003 - 2015 15.7 7.5 32.1
1922 - 2015 17.3 5.1 37.7
2006 - 2015 14.8 7.5 32.1

## Slide 48: Colorado River Runoff (1906-2013 – Green, San Juan, Gila, Gunnison Rivers)
Chart: 
Avg. Runoff (1906-2013) – 15.0 million acre-feet/year (2004-2013) – 13.7 million acre-feet/year
1984 25 million af
1977 5.6 million af

## Slide 49: Colorado River Runoff (1906-2013 – Green, San Juan, Gila, Gunnison Rivers)
Chart: Runoff (million acre-ft.)
Avg. Runoff – 15 million af/yr (1906-2013); 13.7 million af/yr. (2004-2013)
1984 25 million af
Average 15 million af/yr.

## Slide 50: State Water Project Water Allocation
Chart: 
| 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Wet | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.8
Above Normal | 1 | 1 | 1 | 1 | 0.9 | 0.9 | 0.9
Below Normal | 1 | 1 | 1 | 0.65 | 0.5 | 0.65
Dry | 1 | 1 | 1 | 1 | 0.39 | 0.7 | 0.65 | 0.4 | 0.35
Critical | 1 | 0.9 | 1 | 1 | 0.3 | 0.45 | 0.5 | 0.35 | 0.2 | 0.2

## Slide 51
State Water Project Water Allocation
Chart: 
| 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Wet | 1 | 1 | 0.8
Above Normal | 0.9 | 0.9 | 0.9
Below Normal | 0.65 | 0.5 | 0.65
Dry | 0.39 | 0.7 | 0.65 | 0.4 | 0.35
Critical | 0.35 | 0.05 | 0.2 | 0.45
51
5%
20%
Pending
Notes: CVP & SWP Drought Operations Plan (Apr – Nov 2014)
CVP and SWP Water Supplies for 2014 – Based on conditions in late March, DWR expects to maintain a zero allocation for its 29 water contractors. Long‐time water rights holders along the Feather River (“settlement contractors”) would receive 50 percent of their contract water quantities, which is the least amount of water that can be delivered to them under their contracts with DWR. Based on conditions in late March, Reclamation, at this time is not changing its earlier announcement that proposed to provide no supplies to CVP agricultural water service contractors, while Federal wildlife refuges and senior water rights holders along the Sacramento and San Joaquin rivers would receive 40 percent of their contract totals.
Reserves for 2015 – Reclamation estimates that current projected cumulative end of September storages of CVP reservoirs (Shasta, Trinity, and Folsom) will range from about 1.4 maf (90 percent hydrology Drought Operations Plan and Operational Forecast 9 April 8, 2014 with barriers) and 1.9 maf (50 percent hydrology without barriers). Reclamation believes these storages are adequate to meet the 2015 water year needs for the CVP. This assumes implementation of the same drought management actions as specified above. Drier conditions could entail further drought management activities.

## Slide 52
Chart: Exceedance
Cal Water Fix (Alt. 4a)
No Action Alternative (w/ Fall X2 Outflow)
State & Federal Project Supplies
Water Transfer Capability
Drier Period Ability
Wetter Period Ability
Northern Intake | Transfer Capability (50% exceedance)
Without | 224,000 AF
With | 1,148,000 AF
Data represents modeled transfer capability; Seller willingness & actual deliveries not represented
Preliminary State Water Contractor analysis - Subject to Revision
Update
Notes: Northern Intake Transfer Capability (at 50% Exceedance)
Without 224,000 AF (BDCP No Action Alternative (with Fall X2 in 2025 ELT)
With 1,148,000 AF (Cal Water Fix Alt. 4A in 2025 ELT)

## Slide 53: CA Water Fix and the IRP

## Slide 54: IRP Technical Approach State Water Project
Manage flow and export regulations in the near-term
  Continue to engage in collaborative science-based approaches
Pursue a long-term Delta solution
  Continue active participation in the California WaterFix and the California EcoRestore efforts

## Slide 55: 2015 IRP Update Target – SWP Table A + Article 21 Supplies
Chart: Million Acre-Feet
| 2020 | 2025 | 2030 | 2035 | 2040
Min | 228936 | 228936 | 313582 | 313582 | 313582
Max | 1466115 | 1466115 | 1549073 | 1549073 | 1549073
California Water Fix | 984267 | 984267 | 1213358.9011 | 1213358.9011 | 1213358.9011
Assumes Additional Restrictions Starting in 2020
Benefits of the California WaterFix Begin in 2030

## Slide 56: How Does the IRP Perform without the California WaterFix?
Chart: Calendar Year
Blank | 1201749.2418 | 1199919.0879 | 1198088.967 | 1196258.8901 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978
Area | 0 | 0 | 0 | 0 | 147208.8022 | 147208.8022 | 147208.8022 | 147208.8022 | 147208.8022 | 147208.8022 | 147208.8022 | 147208.8022 | 147208.8022 | 147208.8022 | 376300.7033 | 376300.7033 | 376300.7033 | 376300.7033 | 376300.7033 | 376300.7033 | 376300.7033 | 376300.7033 | 376300.7033 | 376300.7033 | 376300.7033
2015 IRP Update Target | 1201749.2418 | 1199919.0879 | 1198088.967 | 1196258.8901 | 984267 | 984267 | 984267 | 984267 | 984267 | 984267 | 984267 | 984267 | 984267 | 984267 | 1213358.9011 | 1213358.9011 | 1213358.9011 | 1213358.9011 | 1213358.9011 | 1213358.9011 | 1213358.9011 | 1213358.9011 | 1213358.9011 | 1213358.9011 | 1213358.9011
The "Do Nothing" Case | 1201749.2418 | 1199919.0879 | 1198088.967 | 1196258.8901 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978 | 837058.1978
Annual Difference 150 TAF on Average
Annual Difference 375 TAF on Average

## Slide 57: MWD Water Resource Strategy Supply/Demand Management–1990 vs. 2035
2035 – 64% Local
1990 – 41% Local
State Water Project (33%)
Colorado River Aqueduct (26%)
Local Surface/Groundwater (34%)
Conservation & Recycling (7%)
Heavy dependence on
imported supplies
Emphasis on conservation, recycling, desalination and local supplies
State Water Project (22%)
Colorado River Aqueduct (14%)
Local Surface/Groundwater (31%)
Conservation & Recycling (33%)

## Slide 58
Chart: 
112,912
Chart: 
| Total Water Use Efficiency | Total Local Supplies | State Water Project | Colorado River
IRP Average Year 2035 | 2168000 | 2082000 | 1490000 | 925000
State WP (22%)
Colorado (14%)
Local Supply (31%)
Conservation & Recycling
(33%)
Chart: 
| Total Water Use Efficiency | Total Local Supplies | State Water Project | Colorado River
1990 | 296407.8799 | 1485024.1534 | 1457676 | 1183250
State WP (33%)
Colorado (27%)
Local Supply (34%)
Conservation & Recycling
(7%)
2035 – 64% Local
1990 – 41% Local
Heavy dependence on
imported supplies
Emphasis on conservation, recycling, local supplies, and transfers
Diversification of Water Portfolio Average Year

## Slide 59: Future Resource Development Costs
Chart: Supply Cost ($/AF)
| Stormwater Centralized | Stormwater Distributed | Groundwater Recovery | Recycled Water | Seawater Desalination
25% | 634 | 3758 | 720 | 1222 | 1859
High | 7387 | 11764 | 2838 | 6059 | 2985
Low | 351 | 1675 | 459 | 526 | 1530
75% | 2012 | 5414 | 1568 | 3224 | 2367
$12,000/AF
* 2015 IRP Update local supply cost analysis as of November 2015, in 2015 dollars
Notes: Local Supply costs are from the 2015 IRP Update, in 2015 dollars.
The vertical lines in the graph represent the low and high unit costs per resource, and the boxed area represents the 25th and 75th percentile values. Data on the in-region resources was compiled in coordination with Metropolitan member agencies, and is based on identified future projects through the 2015 IRP Update project inventory list, stormwater database (developed through the Southern California Water Committee Stormwater Task Force) and project reports. Unit cost estimates include capital and operations and maintenance costs associated with treatment and distribution of the potential water supply. Additional information is included in Appendix 12 of the 2015 IRP Update.
Future projects were analyzed to provide a reasonable range of sample future project costs for each resource type. The analysis includes projects with the status of feasibility, advanced planning, or full design and online before 2025. Outliers were not included in this analysis. Stormwater projects with less than 50 acre-feet of annual yield and recycled water projects with less than 300 acre-feet of annual yield were also not included in this analysis due to an observed resulting deviation from the expected range of values (cost breakpoint of larger unit costs for smaller projects).

## Slide 60: Future Resource Development Costs
Chart: Supply Cost ($/AF)
| Stormwater Centralized | Stormwater Distributed | Groundwater Recovery | Recycled Water | Seawater Desalination
25% | 634 | 3758 | 720 | 1222 | 1859
High | 7387 | 11764 | 2838 | 6059 | 2985
Low | 351 | 1675 | 459 | 526 | 1530
75% | 2012 | 5414 | 1568 | 3224 | 2367
$12,000/AF
* 2015 IRP Update local supply cost analysis as of November 2015, in 2015 dollars
MWD 2016 Tier 1 Treated (with California Water Fix)
~$1,089 to $1,118 / acre-feet
Notes: Local Supply costs are from the 2015 IRP Update, in 2015 dollars.
The vertical lines in the graph represent the low and high unit costs per resource, and the boxed area represents the 25th and 75th percentile values. Data on the in-region resources was compiled in coordination with Metropolitan member agencies, and is based on identified future projects through the 2015 IRP Update project inventory list, stormwater database (developed through the Southern California Water Committee Stormwater Task Force) and project reports. Unit cost estimates include capital and operations and maintenance costs associated with treatment and distribution of the potential water supply. Additional information is included in Appendix 12 of the 2015 IRP Update.
Future projects were analyzed to provide a reasonable range of sample future project costs for each resource type. The analysis includes projects with the status of feasibility, advanced planning, or full design and online before 2025. Outliers were not included in this analysis. Stormwater projects with less than 50 acre-feet of annual yield and recycled water projects with less than 300 acre-feet of annual yield were also not included in this analysis due to an observed resulting deviation from the expected range of values (cost breakpoint of larger unit costs for smaller projects).
MWD Tier 1 Treated with CA Water Fix per email from RJ 4/15/16 at 1242 pm

## Slide 61: California Water Fix Retail Impact – Household Water Costs
Future Supply Improvements | Monthly Impact Per Household
Desalination Focus | $11 / month
Recycling Focus | $7 to 11 / month
Diversified Portfolio (with Cal Water Fix) | Up to $5/month
20 HCF and 50% MWD
Based on analysis completed during IRP process
A diversified portfolio approach strives to meet future supply improvement needs with a cost-effective and reliable mix of local (conservation, recycling, groundwater improvement, desalination), transfers, and imported supplies.
Checking with RJ
Notes: California Water Fix Impacts on Integrated Resource Plan & Financial Analysis
Special Committee on Bay-Delta October 27, 2015
Information from Arnout Van den Berg 10/20/2015
based on Internal Draft dated 7-14-15 - high case + O&M from BDCP Report dated Oct 2013
Financing: 40yr, 6.135%
MWD Share --> 25% 30%
Low High
MWD Share 249 299 2015 M$ per year
Rate Impact @1.75MAF 142 171 2015 $/AF
Rate Impact @2.0MAF 125 150 2015 $/AF
Yield (avg) 378 378 TAF
Unit Cost 660 792 2015 $/AF
Unit Cost + SWP power and treatment 891 1,023 2015 $/AF
2015 T1 Treated Rate w/ BDCP @1.75MAF 1,084 1,113 2015 $/AF
Rate Impact 16% 20%
Annual Rate Impact over 10 yrs 1.6% 2.0%
Retail Rate Impact 50% MWD, 1.75MAF, 20 HUF $ 3 $ 4 per month
Up to $5 per month
Overall Rate Increase w/ WaterFix 3 to 5% per year
Alternatives
Recycling Focus Low High
Unit Cost $ 1,700 $ 2,375 2015 $/AF
Yield 378 378 TAF
Rate Impact 37% 54%
Annual Rate Impact over 10 yrs 3.7% 5.4%
Retail Rate Impact 50% MWD, 1.75MAF, 20 HUF $ 7 $ 11 per month
Desalination Focus
Unit Cost $ 2,367 2015 $/AF
Yield 378 TAF
Rate Impact 53%
Annual Rate Impact over 10 yrs 5.3%
Retail Rate Impact 50% MWD, 1.75MAF, 20 HUF $ 11 per month

## Slide 62: California Water Fix Examples of Alternative Resource Costs
Recycled Water (Existing)
  Edward C. Little Water Recycling Facility 1
    $1,739 /AF
  Orange County Groundwater Replenishment System 2
    $887/AF
  Local Resources Program (average of projects) 3
    $2,240/AF
Recycled Water (Future)
  San Diego Pure Water Project 4
    $1,975/AF to $2,375/AF
Project unit cost from the Local Resources Program FY13/14 reconciliation; grants included in cost
FY09-10 overall project gross unit cost from the GWRS website
Weighted average unit cost from the Local Resources Program FY13/14 reconciliation
Unit costs in 2011 dollars and before grants or netting out avoided costs (from the June 14, 2012, SDCWA Board presentation)
Notes: Edward C Little: Unit cost from LRP FY13/14 reconciliation = $1,739/AF with grants (Kira A)
GWRS: 2009-2010 cost summary (65,950 AF per year) overall project gross cost = $887/AF (from website); includes adding back in OCSD capital contribution and outside grants; Kira received updated numbers (FY2014-15) from OCWD, which shows a higher annual cost, but also a higher production (76,563 AF per year) for an overall lower unit cost (roughly calculates to ~$810/AF)
LRP: Weighted average (based on production) unit cost for 2014 (from the FY13-14 reconciliation) = $2,240/AF; does not include outliers
If only analyze projects that started operation in the last 10 years, the weighted average unit cost = $3,623/AF due to the ramp up (low initial production) (Kira A)
Pure Water Project: Unit costs in 2011 dollars and before grants or netting out avoided costs (from the June 14, 2012, SDCWA Board presentation); higher number may include a $275 incentive. Note from Warren T: the folks from The City of San Diego objected to how the SDCWA was portraying the City of SD RWS project costs. The City of San Diego Water Purification Demonstration Project Report Final Draft (March 2013) listed a unit cost of $2,000/AF (AWP facility, pipeline system, source control, public outreach), which includes LRP credits of $275/AF and 20% grant funding of capital costs (page 112) and based on 15MGD (16,800 AF per year)

## Slide 63: California Water Fix Examples of Alternative Resource Costs
Seawater Desalination
  Carlsbad Desalination Project 1
    $2,367/AF
Groundwater Recovery
  Local Resources Program (average of projects) 2
    $1,157/AF
Estimated unit cost from the June 9, 2012, SDCWA Board presentation
Weighted average unit cost from the Local Resources Program FY13/14 reconciliation
Notes: Carlsbad: From presentation given at a June 9, 2015, Board meeting on SDCWA’s budget. Water purchase price Poseidon Water Purchase Agreement = $2,367/AF (2016 current estimate). Production yield = 48,000 AF per year. [Warren T]
Groundwater Recovery: Weighted average (based on production) unit cost for 2014 (from the FY13-14 reconciliation) = $1,157/AF; does not include outliers. Includes projects that are over 20 years in production. If only analyze projects that started operation in the last 10 years, the weighted average unit cost = $1,336/AF. Future desalter (new LRP application) much more expensive [Kira A]
Potential for groundwater recovery: Largest future project identified in the IRP project inventory list is 24,000 AF per year (Tujunga Well Treatment)

## Slide 64
State Project Water
Colorado
Water
Blend ing
Zone
MWD SWP Supplies | Blending
Existing (Avg. Yr.) | Met
BDCP Preferred Alt | Met
Delta No Fix (Avg. Yr.) | Sometimes
Delta No Fix (Below Normal) | Rarely
Blending
Zone
California WaterFix allows MWD blending goals to be met
Notes: Metropolitan’s SWP Supplies Supplies Blending
Existing 1,200,000 AFY Met
BDCP Preferred Alt. 1.2 – 1,400,000 AFY Met
Delta No Fix (Avg Yr) 875,000 AFY Sometimes
Delta No Fix (Below Normal) ~675,000 AFY Rarely
Blending Target Requirements
~50% SWP Allocation to meet blend targets 950,000 AFY
~35% SWP Table A to cover Exclusive Zones 665,000 AFY
ASSUMPTIONS
• BDCP no fix scenario = 3.5 maf/yr SWP/CVP; MWD is 1/4 or 850,000 af/year ON AVERAGE - LONG-TERM!!!!!
• 850,000 AF to MWD represents 44.5% of SWP Table A (i.e. this is the new long-term baseline)
• No SWP banking and suface water accounts to use for blending (i.e. only for reliability)
• Reliability is number 1 priority; Blending and meeting TDS targets is a secondary priority
• MWD needs a 50% SWP allocation needed to meet blend targets; or 1.9 maf x 50% = 950,000 AF
• MWD needs about 35% to cover exclusives, then we can blend (or 35% x 1.9 maf = 665,000 AF/yr)
• MWD needs 16% allocations (or 300,000 AF) to meet blending goals
• SWP minimum to consider starting to blend = 37% allocation or 707,000 AF
• Runoff indexes -- Critical, Dry, Below Normal, Above Normal, Wet
• Runoff indexes = Critical-16%, Dry-16%, BN-16%, AN-15%, Wet-35% (based on historical Sac 4-River Runoff Index)
THEREFORE
• Unless runoff is above average, you cannot meet blending needs.
DEVELOP CHARTS & MEMBER AGENCY PERCENTAGE MATRICES
• Scenario 1: Existing SWP/CVP Supplies (4.7 MAF/4 = 1.2 MAF on average) -- Blending goals met, show CRA area, SWP area, blending area
• Scenario 2: BDCP No Fix with Avg Yr runoff (3.5 MAF/4 = 850 TAF or 1.7 maf minus 50%) -- 100% of the time you will not need meet blending goals (i.e. only partial blending allowed in a smaller portion of MWD service area)
• Scenario3: BDCP No Fix with Below Normal Yr runoff (665 TAF or 1.7) -- 22% of time you cannot do any blending [(850,000-665,000)/850,000 = 22%; assumes linear relationship with runoff index]
MWD Water Quality Treatment Plants
Normal operating conditions (Nov 04-Oct 13) (Average) SWP CRA
Jensen 100% 0%
Weymouth 41% 59%
Diemer 39% 61%
Mills 100% 0%
Skinner 39% 61%

## Slide 65: Summary
Cal Water Fix is less costly than shortages or other alternatives
The do nothing approach is not sustainable
With Cal Water Fix, rate impacts will be less than other resource alternatives and households will spend less
Notes:   We have good estimates of the cost and the increased water supply benefits of the of the California Water Fix
    $X Billion and Y acre-feet, approximately $X/acre-foot
  $X/acre-foot is significantly cheaper than shortages or other alternatives
    These come in between $Z and $Z per acre-foot
  Because the California Water Fix is cheaper, MWD rate impacts will be less than the alternatives and households will spend less for a reliable water supply

## Slide 66: EcoRestore

## Slide 67: California EcoRestore Projects Estimated Acreage
SWP/CVP Bio Op Mandates (25,000 acres)
  Floodplain Restoration 17,000 ac
  Tidal Habitat 8,000 ac
State Proposition 1 Grants (5,000 acres)
  Floodplain Restoration 500 ac
  Managed Wetlands 3,500 ac
  Tidal Habitat 1,000 ac
Notes: California EcoRestore is an initiative to help coordinate and advance at least 30,000 acres of critical habitat restoration in the Sacramento – San Joaquin Delta over the next four years. Driven by world-class science and guided by adaptive management, California EcoRestore will aggressively pursue habitat restoration projects with clearly defined goals, measurable objectives, and financial resources to help ensure success.
A broad range of habitat restoration projects will be pursued, including projects to address aquatic, sub-tidal, tidal, riparian, flood plain, and upland ecosystem needs.
California EcoRestore’s initial goal is to advance (i.e. complete or break ground on) 30,000 acres of Delta habitat restoration:
25,000 acres associated with existing mandates for habitat restoration, pursuant to federal biological opinions. These projects will be funded exclusively by the state and federal water contractors that benefit from the State Water Project and the Central Valley Project systems.
5,000 acres of habitat enhancements. Proposition 1 grants to local governments, non-profit organizations, and other entities will support these habitat enhancements throughout the Delta. Funding will come primarily from the Delta Conservancy, the California Department of Fish and Wildlife, and the California Department of Water Resources.
California EcoRestore is unassociated with any habitat restoration that may be required as part of the construction and operation of new Delta water conveyance (California WaterFix).
California EcoRestore Funding
Costs for California EcoRestore are expected to reach at least $300 million in the first four years. Much of these costs will be borne by the state and federal public water agencies currently required to mitigate the ecological impacts of the State Water Project and the Central Valley Project in the Delta.
Funding for habitat enhancements unassociated with mitigation will come primarily from Propositions 1 and 1E, the AB 32 Greenhouse Gas Reduction Fund, and local, federal, and private investment.
More information on California EcoRestore is available through the links below:
EcoRestore Fact Sheet http://resources.ca.gov/ecorestore/

## Slide 68: California EcoRestore Projects Estimated Acreage
SWP/CVP Bio Op Mandates (25,000 acres)
  Floodplain Restoration (17,000 ac) ~$719 M
  Tidal Habitat (8,000 ac) ~$235 M
State Proposition 1 Grants (5,000 acres)
  Floodplain Restoration (500 ac) ~$21 M
  Managed Wetlands (3,500 ac) ~$40 M
  Tidal Habitat (1,000 ac) ~$29 M
Notes: California EcoRestore is an initiative to help coordinate and advance at least 30,000 acres of critical habitat restoration in the Sacramento – San Joaquin Delta over the next four years. Driven by world-class science and guided by adaptive management, California EcoRestore will aggressively pursue habitat restoration projects with clearly defined goals, measurable objectives, and financial resources to help ensure success.
A broad range of habitat restoration projects will be pursued, including projects to address aquatic, sub-tidal, tidal, riparian, flood plain, and upland ecosystem needs.
California EcoRestore’s initial goal is to advance (i.e. complete or break ground on) 30,000 acres of Delta habitat restoration:
25,000 acres associated with existing mandates for habitat restoration, pursuant to federal biological opinions. These projects will be funded exclusively by the state and federal water contractors that benefit from the State Water Project and the Central Valley Project systems.
5,000 acres of habitat enhancements. Proposition 1 grants to local governments, non-profit organizations, and other entities will support these habitat enhancements throughout the Delta. Funding will come primarily from the Delta Conservancy, the California Department of Fish and Wildlife, and the California Department of Water Resources.
California EcoRestore is unassociated with any habitat restoration that may be required as part of the construction and operation of new Delta water conveyance (California WaterFix).
California EcoRestore Funding
Costs for California EcoRestore are expected to reach at least $300 million in the first four years. Much of these costs will be borne by the state and federal public water agencies currently required to mitigate the ecological impacts of the State Water Project and the Central Valley Project in the Delta.
Funding for habitat enhancements unassociated with mitigation will come primarily from Propositions 1 and 1E, the AB 32 Greenhouse Gas Reduction Fund, and local, federal, and private investment.
More information on California EcoRestore is available through the links below:
EcoRestore Fact Sheet http://resources.ca.gov/ecorestore/

## Slide 69: Delta Emergency Preparedness Plan and Progress

## Slide 70: Overview of Plan Status
Planning Schedule
  Interim Plan – 2007
  Draft Plan – 2014
  Final Plan – 2017
Implementation Schedule
  Initial concepts (2006-08)
  Place initial rock stockpiles (2007-08)
  DWR Emergency Plan w/Corps (2008-13)
  DWR additional stockpiles (2015-17)
  RDs construct pathway levee improvements (2011-16)
Notes: Recent levee failures resulting from Hurricane Katrina have increased the awareness of the risk of catastrophic failure of California’s Sacramento-San Joaquin Delta (Delta) levee system leading to the potential loss of the Delta as a drinking water supply for major population centers in the San Francisco Bay area and Southern California. The Department of Water Resources (DWR) has testified that a Delta levee system failure might not fully recover from a hypothetical 6.5 Richter scale earthquake near the western Delta. This is a relatively remote, but high consequence event, leading simultaneously to 50 levee breaches and the flooding of 20 Delta islands. The range of risks will ultimately be an output of the Delta Risk Management Strategy. In February 2006, the Board directed and staff has responded with a Delta emergency preparedness and response plan to avert the catastrophic loss of Delta water supplies resulting from this type of severe emergency. This plan minimizes water supply impacts with the most cost-effective means of prevention and response.
Both pre-event and post-event strategies described below, require the dilution of saltwater trapped in Delta islands by diverting additional Sacramento River flows to re-establish a freshwater pool in the central Delta.
Pre-event Strategy
A pre-event strategy would involve advance construction of levee and river flow barriers to block salt water from entering the south Delta in a major emergency, while isolating saltwater in the central Delta where it can be flushed seaward by the freshwater pool. A pre-event approach could be developed in about three years at costs from $330 million to $485 million, allowing exports to be resumed around two months after the emergency event.
Post-event Strategy
The preferred post-event strategy allows saltwater to enter the entire Delta followed by the creation of an emergency freshwater pathway through existing channels from the central Delta to the export pumps. Feasibility cost estimates for this strategy are about $50 million to pre-position materials and equipment in advance of an emergency, so that pathway development can be substantially unconstrained by other emergency work in the Delta. Costs could increase to a total of approximately $200 million, if and when an emergency takes place and depending on the scale of the actual emergency event. By considering a variety of response priorities, it was concluded that water exports could be operational and reasonably functional in about six months under this strategy. Although somewhat longer than the pre-event strategies, it is still considered an acceptable time frame.
The time to resume exports is highly sensitive to levee breach lengths, which influence levee repair times and response priorities. For smaller breaches, critical life and property needs may be able to proceed ahead of the emergency freshwater pathway development, while still developing the pathway in the above time frame. For much larger and less likely breaches, the pathway would have to be developed in parallel with other emergency response needs in the Delta to be operational in the six-month period, and would be critically dependent on the availability and use of stockpiled materials. It should be noted that this plan responds to an extreme emergency, but can be adapted in scale to smaller events.
DWR is working with Metropolitan and the State Water Contractors (SWC) to integrate these water supply protections into an interim report to the Emergency Operations Plan for the Delta over the next two months. This will more fully define the pre-positioning of stockpiles, improved emergency contracting capabilities and response mechanisms for a severe levee failure emergency. These plans do not constitute a reliable long-term water conveyance strategy in the Delta, which will be developed through the comprehensive planning of the Delta Vision Process and the Bay-Delta Conservation Plan.
Propositions 1E and 84 both contain funds which could be used for the purposes outlined in this board letter.
Some costs may not be covered by Propositions 1E and 84 funds and may be attributed to the State Water Project.
In that event, Metropolitan would be responsible for its share of those costs.

## Slide 71
Emergency Freshwater Pathway

## Slide 72: Freshwater Pathway Status
Improvements meet seismic preparedness needs
Improvements ongoing
Improvements needed

## Slide 73: DWR Emergency Management Reports
Released: April 2007
Released: June 2012
Released: April 2014

## Slide 74: Delta Flood Emergency Management
Coordinated Cal OES, USACE, DWR, County and local response
  Integral to Cal OES Northern CA Catastrophic Flood Management Plan
  Memorandum of Agreement synthesizes DWR/USACE operations
Pathway developed if island flooding and salinity intrusion is extensive
  Restores exports by repairing levees and constructing channel barriers along Middle River
Released: April 2014
Notes: Recent levee failures resulting from Hurricane Katrina have increased the awareness of the risk of catastrophic failure of California’s Sacramento-San Joaquin Delta (Delta) levee system leading to the potential loss of the Delta as a drinking water supply for major population centers in the San Francisco Bay area and Southern California. The Department of Water Resources (DWR) has testified that a Delta levee system failure might not fully recover from a hypothetical 6.5 Richter scale earthquake near the western Delta. This is a relatively remote, but high consequence event, leading simultaneously to 50 levee breaches and the flooding of 20 Delta islands. The range of risks will ultimately be an output of the Delta Risk Management Strategy. In February 2006, the Board directed and staff has responded with a Delta emergency preparedness and response plan to avert the catastrophic loss of Delta water supplies resulting from this type of severe emergency. This plan minimizes water supply impacts with the most cost-effective means of prevention and response.
Both pre-event and post-event strategies described below, require the dilution of saltwater trapped in Delta islands by diverting additional Sacramento River flows to re-establish a freshwater pool in the central Delta.
Pre-event Strategy
A pre-event strategy would involve advance construction of levee and river flow barriers to block salt water from entering the south Delta in a major emergency, while isolating saltwater in the central Delta where it can be flushed seaward by the freshwater pool. A pre-event approach could be developed in about three years at costs from $330 million to $485 million, allowing exports to be resumed around two months after the emergency event.
Post-event Strategy
The preferred post-event strategy allows saltwater to enter the entire Delta followed by the creation of an emergency freshwater pathway through existing channels from the central Delta to the export pumps. Feasibility cost estimates for this strategy are about $50 million to pre-position materials and equipment in advance of an emergency, so that pathway development can be substantially unconstrained by other emergency work in the Delta. Costs could increase to a total of approximately $200 million, if and when an emergency takes place and depending on the scale of the actual emergency event. By considering a variety of response priorities, it was concluded that water exports could be operational and reasonably functional in about six months under this strategy. Although somewhat longer than the pre-event strategies, it is still considered an acceptable time frame.
The time to resume exports is highly sensitive to levee breach lengths, which influence levee repair times and response priorities. For smaller breaches, critical life and property needs may be able to proceed ahead of the emergency freshwater pathway development, while still developing the pathway in the above time frame. For much larger and less likely breaches, the pathway would have to be developed in parallel with other emergency response needs in the Delta to be operational in the six-month period, and would be critically dependent on the availability and use of stockpiled materials. It should be noted that this plan responds to an extreme emergency, but can be adapted in scale to smaller events.
DWR is working with Metropolitan and the State Water Contractors (SWC) to integrate these water supply protections into an interim report to the Emergency Operations Plan for the Delta over the next two months. This will more fully define the pre-positioning of stockpiles, improved emergency contracting capabilities and response mechanisms for a severe levee failure emergency. These plans do not constitute a reliable long-term water conveyance strategy in the Delta, which will be developed through the comprehensive planning of the Delta Vision Process and the Bay-Delta Conservation Plan.
Propositions 1E and 84 both contain funds which could be used for the purposes outlined in this board letter.
Some costs may not be covered by Propositions 1E and 84 funds and may be attributed to the State Water Project.
In that event, Metropolitan would be responsible for its share of those costs.

## Slide 75: Policies/Processes

## Slide 76: Metropolitan Board Policies & Agreements
Policies
  Delta Action Plan Framework Jun 2007
  Delta Conveyance Criteria Sep 2007
  Delta Governance Principles Aug 2008
  Delta Vision Implementation Jan 2009
  Delta-Related Legislation Apr 2009
Funding Agreements
  Execution of Planning Agreement for BDCP Oct 2006
  Execution of BDCP Cost-Sharing Agreement Nov 2006
  Execution of Initial Funding Agreement Dec 2008
  Execution of Amendments to Planning Agmt Dec 2009
  Execution of Amendment (additional funds) July 2010
  Execution of Amendment to MOA Aug 2011

## Slide 77: Metropolitan Board Actions Delta Conveyance Criteria (Sep 2007)
Provide Water Supply Reliability | Consistent with DWR’s State Water Project Reliability Report (2005)
Improve Export Water Quality | Reduce bromide and dissolved organic carbon concentrations
Allow Flexible Pumping Operations in a Dynamic Fishery Environment | Allow the greatest flexibility in meeting water demands by taking water where and when it is least harmful to migrating salmon and in-Delta fish species Reduce inherent conflict between fisheries & water conveyance
Enhance Ecosystem Fishery Habitat Throughout Delta | Provide ability to restore fishery habitat throughout the Delta Minimize disruption to tidal food web processes Provide for fluctuating salinity levels
Reduce Seismic Risks | Provide significant reductions in risks to export water supplies from seismic-induced levee failure and flooding
Reduce Climate Change Risks | Reduce long-term risks from salinity intrusion associated with rising sea levels Intake locations should be able to withstand an estimated 1- to 3-foot sea-level rise in the next 100 years

## Slide 78: California WaterFix Summary of Planning Process
2006 – 2009
BDCP Stakeholder Steering Committee formed
Planning Agreement signed
Alternative scoping, modeling, environmental analysis, etc.
2010 – 2011
1st Administrative Draft BDCP released to the public
Admin Draft EIR/S Chapters posted online
2012
2nd Administrative Draft BDCP released to the public
2013 - 2014
First Public Draft EIR/S & Draft BDCP released to the public
228 day comment period (Dec 13, 2013 – Jul 29, 2014)
2015
Partially Recirculated DEIR & Supplemental DEIS released
112 day comment period (July 10 – October 30, 2015)

## Slide 79: Diverse Alternatives Analyzed
1930-50s
Various seawater barriers (Biemond Plan, Reber Plan, etc.)
1960-70s
Chipps Island barrier
1980s
Peripheral canal + SB200
1990-2000s
Recent
Peripheral canal (21,800 cfs)
Through-Delta
Duke’s Ditch (Through-Delta)
South & North Delta Programs
Bay Delta Accord
CALFED Plan (~ 19 alternatives, storage, etc.)
Post-CALFED Thru-Delta focus (>26 alternatives)
BDCP - Multiple Initially Screened & 16 EIR/S Alts

## Slide 80: Water Quality

## Slide 81
California WaterFix
Improves Water Quality
27% salinity reduction
Colorado River
650 mg/l
Sacramento River
100 mg/l
SWP (Existing)
302 mg/l
SWP (Cal Water Fix) 221 mg/l
(27% improvement)
San Joaquin River
320 mg/l
Sacramento, San Joaquin & Colorado River water quality represents historical average annual recorded data
State Water Project water quality is a comparison of modeled data from the Recirculated Draft EIR/EIS
Notes: Recirculated Draft EIR/S Water Quality Modeling Results
Average Salinity at Banks PP for Alternative 4A
Existing Conditions (EC, µmhos/cm) Alternative 4A (EC, µmhos/cm) % Improvement
All Water years 530 388 27%
Drought conditions 646 491 24%
81

## Slide 82
Colorado River
0.06 mg/l
Sacramento River
0.02 mg/l
SWP (Existing)
0.36 mg/l
SWP (Cal Water Fix) 0.22 mg/l
(37% improvement)
Sacramento, San Joaquin & Colorado River water quality represents historical average annual recorded data
State Water Project water quality is a comparison of modeled data from the Recirculated Draft EIR/EIS
San Joaquin River
0.1 – 0.4 mg/l
California WaterFix
Improves Water Quality
37% bromide reduction
Notes: Source: Appendix B. Supplemental Modeling Results for New Alternatives, Table EC-2.
RDEIR/S Water Quality Modeling Results
Average Bromide at Banks PP for Alternative 4A
Existing Conditions (µg/L) Alternative 4A (µg/L) % Improvement
All Water years 356 224 37%
Drought conditions 469 319 32%
Source: Appendix B. Supplemental Modeling Results for New Alternatives, Table Br-2.
Notes:
The data in these tables are summarized modeling results from the water quality modeling studies conducted to evaluate water quality effects of the BDCP/California Water Fix. The average concentrations are modeling results and are not actual conditions. Focus on the percent reduction as more informative.
Sacramento River at Greene’s Landing 0.018 mg/L average annual historical sampled data
Bromide at the Banks Pumping Plant has averaged 0.230 mg/L in recent years (1990-2006). -- http://www.waterboards.ca.gov/rwqcb5/water_issues/drinking_water_policy/salinity_conceptual_model/pgs13_27.pdf
82

## Slide 83
State Project Water
Colorado
Water
Blend ing
Zone
MWD SWP Supplies | Blending
Existing (Avg. Yr.) | Met
BDCP Preferred Alt | Met
Delta No Fix (Avg. Yr.) | Sometimes
Delta No Fix (Below Normal) | Rarely
Blending
Zone
California WaterFix allows MWD blending goals to be met
Notes: Metropolitan’s SWP Supplies Supplies Blending
Existing 1,200,000 AFY Met
BDCP Preferred Alt. 1.2 – 1,400,000 AFY Met
Delta No Fix (Avg Yr) 875,000 AFY Sometimes
Delta No Fix (Below Normal) ~675,000 AFY Rarely
Blending Target Requirements
~50% SWP Allocation to meet blend targets 950,000 AFY
~35% SWP Table A to cover Exclusive Zones 665,000 AFY
ASSUMPTIONS
• BDCP no fix scenario = 3.5 maf/yr SWP/CVP; MWD is 1/4 or 850,000 af/year ON AVERAGE - LONG-TERM!!!!!
• 850,000 AF to MWD represents 44.5% of SWP Table A (i.e. this is the new long-term baseline)
• No SWP banking and suface water accounts to use for blending (i.e. only for reliability)
• Reliability is number 1 priority; Blending and meeting TDS targets is a secondary priority
• MWD needs a 50% SWP allocation needed to meet blend targets; or 1.9 maf x 50% = 950,000 AF
• MWD needs about 35% to cover exclusives, then we can blend (or 35% x 1.9 maf = 665,000 AF/yr)
• MWD needs 16% allocations (or 300,000 AF) to meet blending goals
• SWP minimum to consider starting to blend = 37% allocation or 707,000 AF
• Runoff indexes -- Critical, Dry, Below Normal, Above Normal, Wet
• Runoff indexes = Critical-16%, Dry-16%, BN-16%, AN-15%, Wet-35% (based on historical Sac 4-River Runoff Index)
THEREFORE
• Unless runoff is above average, you cannot meet blending needs.
DEVELOP CHARTS & MEMBER AGENCY PERCENTAGE MATRICES
• Scenario 1: Existing SWP/CVP Supplies (4.7 MAF/4 = 1.2 MAF on average) -- Blending goals met, show CRA area, SWP area, blending area
• Scenario 2: BDCP No Fix with Avg Yr runoff (3.5 MAF/4 = 850 TAF or 1.7 maf minus 50%) -- 100% of the time you will not need meet blending goals (i.e. only partial blending allowed in a smaller portion of MWD service area)
• Scenario3: BDCP No Fix with Below Normal Yr runoff (665 TAF or 1.7) -- 22% of time you cannot do any blending [(850,000-665,000)/850,000 = 22%; assumes linear relationship with runoff index]
MWD Water Quality Treatment Plants
Normal operating conditions (Nov 04-Oct 13) (Average) SWP CRA
Jensen 100% 0%
Weymouth 41% 59%
Diemer 39% 61%
Mills 100% 0%
Skinner 39% 61%

## Slide 84: California WaterFix is important for groundwater storage
Bay Delta provides high quality water
Essential to reduce salt impacts
Critical for groundwater storage
Orange
County
Main
San Gabriel
Raymond
Chino
San Jacinto
Las Posas
Cuchamonga
Warner Valley
Elsinore
Upper San Juan
San Mateo & San Onofre
Six Basins
Sylmar
Verdugo
East San
Fernando
84
Notes: Supply Salt (TDS mg/l) Salt (Lbs / acre ft)
Colorado River ~ 500 to 700 mg/l 1,360 to 1,900 lbs/af
Bay Delta (current) ~ 300 mg/l 700 lbs/af
Bay Delta (new conveyance) ~ 200 mg/l 470 lbs/af
Objectives
Improve export quality to meet Public Health standards & reduce treatment costs
Support actions to minimize salinity imports
Meet 500 mg/l blending goal
Some Basin Plans have low TDS objectives that could restrict extended recharge of high salinity Colorado River water *
Salinity Management Policy (Board Policy March 1999)
Protect imported quality and seek salinity reductions
Establish total dissolved solids objective of < 500 (mg/L)
Optimize the long-term use of Colorado River water in conjunction with State Water Project supplies
Make the Salinity Management Action Plan the primary strategy to carry out this policy
Support actions to minimize salinity imports to enhance groundwater and recycled water programs
Regional Board Basin Plans have TDS water quality objectives for groundwater. Raymond and Main San Gabriel Basins objectives are at 450 mg/L TDS, the eastern portions of San Fernando Basin range from 400 to 600 mg/L. Some parts of Chino Basin have TDS objectives in the 200-300 mg/L range. Central Basin is higher at 700 mg/L. Orange Co Basin is 580 mg/L.

## Slide 85: Delta Wetlands

## Slide 86
86
Preliminary Subject to Revision
Tunnels
San Joaquin River
Through Delta
CVP Pumps
SWP Pumps
Sacramento
Stockton
Sac River
West Canal
East Canal
SWP Pumps
CVP Pumps
Regional Map
Chipps Island
Bouldin Island
Webb Tract
Holland Tract
Bacon Island
Notes: 86

## Slide 87
Chipps Island
Bouldin Island
Location Map
Webb Tract
Holland Tract
Bacon Island
87
Hwy 12

## Slide 88: Other Tunnel/ Infrastructure Projects

## Slide 89: Large Diameter Tunnels International
51 ft. – Shanghai, China Yangtze River highway tunnel; 2 bores
33 ft. – Nagarjuna Sagar NP, India 27 mile water supply tunnels
41 ft. – Jinping, China 40 mile hydroelectric tunnels
44 ft. – Kuala Lumpur, Malaysia Dual-deck transportation/stormwater
Updating
Notes: Other tunnels: 51 ft. – Shanghai, China Yangtze River highway tunnel; 2 bores
Chicago tunnels address combined sewer and runoff overflow from being dumped (and polluting) Lake Michigan. EPA rule requires they hold the water and run it through their treatment plant. The 109 miles of 30 foot tunnels and smaller tunnels are used as a storage reservoir until it can be treated. Robbins Company had 18 TBMs out of the 30 TBMs in Chicago. Chicago soil is all limestone
Cleveland tunnels 1997 to 2008
Alp Transit Tunnels – 2 bores; 30 ft diameter; 56 miles long; High speed rail; 5 TBMs

## Slide 90: Large Diameter Tunnels United States
30 ft. – Chicago, USA 109 mile sewer overflow tunnel 30 tunnel boring machines
24 to 45 ft. – Cleveland, USA Sewer overflow tunnels
Updating
Notes: Other tunnels: 51 ft. – Shanghai, China Yangtze River highway tunnel; 2 bores
Chicago tunnels address combined sewer and runoff overflow from being dumped (and polluting) Lake Michigan. EPA rule requires they hold the water and run it through their treatment plant. The 109 miles of 30 foot tunnels and smaller tunnels are used as a storage reservoir until it can be treated. Robbins Company had 18 TBMs out of the 30 TBMs in Chicago. Chicago soil is all limestone
Cleveland tunnels 1997 to 2008
Alp Transit Tunnels – 2 bores; 30 ft diameter; 56 miles long; High speed rail; 5 TBMs

## Slide 91
Project | Cost | Population Served | Per Capita
MWD Diamond Valley Lake/Inland Feeder | $3,100,000,000 | 18,000,000 | $172
EBMUD Freeport Project | $517,000,000 | 1,300,000 | $398
SDCWA Emergency Storage Project | $1,500,000,000 | 2,800,000 | $536
BDCP Conveyance (BDCP Draft EIR/S) | $14,990,000,000 | 25,000,000 | $600
CCWD Los Vaqueros Project | $570,000,000 | 550,000 | $1,036
SWP Coastal Aqueduct & CCWA Project | $575,000,000 | 430,000 | $1,337
SFPUC’s Hetch-Hetchy Improvement Project | $4,800,000,000 | 2,500,000 | $1,920
BDCP Economic Benefits and Financial Strategies, SCWC/The PFM Group, February 2012
Statewide Comparison of Water Improvement Projects
Notes: Metropolitan’s Diamond Valley Reservoir/Inland Feeder project is primarily an emergency storage facility but also provides drought and water quality benefits. The population of Metropolitan’s service area was 18 million people when water started flowing into Diamond Valley Lake in 1999.
East Bay Municipal Utilities District Freeport Project is primarily a water supply reliability project for Alameda and Contra Costa Counties with supplemental CVP supplies.
SDCWA Emergency Storage Project is being built to enhance reliability of the water supply of San Diego in the event of seismic disruption.
Bay Delta Conservation Plan Conveyance Facility
Contra Costa Water District’s Los Vaqueros Project is a reservoir to improve water quality and provide emergency storage ( currently the Phase 2 expansion to 160,000 acre-feet is under construction)
SWP Coastal Aqueduct and Central Coast Water Authority Project, which consist of SWP conveyance and treatment facilities for San Luis Obispo and Santa Barbara Counties.
San Francisco Public Utilities Commission’s Hetch Hetchy Project is being repaired to protect against future seismic events, current building codes and drinking water regulations

## Slide 92
The Delta
Sacramento
Stockton
Suisun Bay
State & Federal Pumping Plants
92

## Slide 93: Backups

## Slide 94
Month | Old & Middle River Criteria (Scenario 6) | BDCP Preferred Alternative |  | California WaterFix Preferred Alt.
 |  | Alt. 4-H3 | Alt. 4-H4 | Alt. 4A
Oct - Nov | No diversion during pulse flow -5,000 cfs in Nov | - 313,000 af | - 231,000 af | - 313,000 af
Dec - Mar | -5,000 to -3,000 cfs | -454,000 af | - 379,000 af | -454,000 af
Apr - May | -2,000 to +3,000 cfs | -60,000 af | - 51,000 af | -60,000 af
Jun | - 3,500 to + 1,000 cfs | -113,000 af | - 95,000 af | -113,000 af
Jul – Sep | No flow restrictions | +26,000 af | +89,000 af | +26,000 af
 | TOTAL Annual Impacts | - 914,000 af | - 667,000 af | - 914,000 af
Delta Conveyance
Additional Old & Middle River Reverse Flow Restrictions
Information produced by CH2M; Scenario 6 Breakdown

## Slide 95: Cost Allocation Alternatives

## Slide 96: State Water Project BDCP Cost Allocation Alternatives
SWP ‘Table A’ Contract Approach | 
Cost Allocation | SWP “Table A” contract Except for North of Delta contractors
Water Allocation | SWP Table A amounts
Description | Provides for reduced participation for North of Delta only Includes provisions for contractor-to-contractor annual/multi-year transfers, and exchange programs Contract amendment likely needed to reflect different cost allocations, supply deliveries, and transfer/exchange provisions
Summary & Issues | Allocation similar to existing contract approach Obligation of individual agency to work out water transfer and exchange agreements
96
Notes: The first methodology would require DWR maintain two sets of SWP accounting to determine Table A allocations with and without the conveyance facility (Project). Several challenges exist that increase the complexity of this method. For example, should separate SWP reservoir storage conditions be tracked for the with and without Project conditions? How would one consider future changes in regulatory criteria absent the Project?

## Slide 97: State Water Project BDCP Cost Allocation Alternatives
Subscribed Capacity Approach | 
Cost Allocation | Contractors subscribe to Delta tunnel capacity Except for North of Delta contractors
Water Allocation | Subscribe for tunnel capacity based on water supply needs Remaining water supply benefits reallocated through transfers/exchanges
Description | Includes provisions for contractor-to-contractor annual/multi-year transfers, and exchange programs Contract amendment likely needed to reflect different cost allocations, supply deliveries, and transfer/exhange provisions
Summary & Issues | Those who don’t fully participate face unreliable thru-Delta supplies due to regulations or catastrophic events More reliable water transfers through tunnel facility More access to unregulated or flood flows through tunnel
97
Notes: Level of Participation Alternative (2D) - The second methodology would use a fixed formula that would be negotiated and established at the onset of conveyance operation. Challenges with this method include the fact that a fixed formula, even based on year type, would not fully capture the variation shown in the model results.
Alternative 2D is a two-part approach to BDCP Cost allocation that allows SWP contractors to “opt-in” to the level of participation that they desire and also provides individual SWP contractors with the management tools that allow them to develop their own Integrated Water Management Programs in a way that optimizes water supply benefits and results in affordable costs. Alternative 2D includes two parts:
Allocation of participation in BDCP on a subscription basis for SWP contractors with individual contractors able to request as much or as little of available BDCP capacity as needed;
A Water Management framework that allow for the flexible use of all allocated water supply
Contract Amendments – The operational differences between participants and non-participants would likely require contract amendments for both parties clearly stating what each party is obligated to pay and what benefits they may receive.
Article 21 and Transfers – The conveyance facility may impact how much Article 21 water is available, how much conveyance capacity would be available to facilitate water transfers and if carriage water losses need to be calculated for transferred water. In the case that more water is available due to the facility, decisions are needed regarding how non-participants have access to that water and what fees they may need to pay.
Through-Delta Conveyance Capability – Though the participants would continue to rely, partially, on the Delta channels for conveyance, participants would rely mainly on the new conveyance facility and may not want the obligation of paying to maintain and/or improve the ability of the SWP to convey water through the Delta.

## Slide 98: Key in Determination of Alternative Contractor’s Participation May Determine Best Alternative
 | Participation |  |  |  | Participation |  | 
 | 0 % | 100 % | 200 % |  | 0 % | 100 % | 200 %
Contractor 1 |  |  |  |  |  |  | 
Contractor 2 |  |  |  |  |  |  | 
Contractor 3 |  |  |  |  |  |  | 
Contractor 4 |  |  |  |  |  |  | 
Contractor … |  |  |  |  |  |  | 
Contractor … |  |  |  |  |  |  | 
Table ‘A’ Contract Approach
Subscribed Capacity Approach
98

## Slide 99: Metropolitan Water District Cost Allocation “Example”
 | No BDCP | 100% Participation | 110% Participation
Existing SWP Charge | $495 mill | $495 mill | $495 mill
Incremental BDCP Charge | $0 mill | $412 mill | $453 mill
Total | $495 mill | $907 mill | $948 mill
Average SWP Deliveries | 960,500 af | 960,500 af | 960,500 af
Incremental BDCP | 0 af | 431,000 af | 474,000 af
Total | 960,500 af | 1,391,500 af | 1,434,500 af
Existing SWP Charge | $ 515 /af | $ 515 /af | $ 515 /af
Incremental BDCP Charge | -- | $ 956 /af | $ 956 /af
Total | $ 515 /af | $ 652 /af | $ 661 /af
Rate impact August 2013 analysis: 1.5% to 2% per year for 10 years ($138 to $166 per acre feet increase)
BDCP costs preliminary; Existing SWP costs based on 2014-15 Statement of Charges includes power and O&M
Water supply based on DWR CALSIM modeling of average Table A & incremental BDCP allocations
99
MWD Tier 1 Treated ($847/af) with Delta Improvements = $985 to $1,013/AF
Notes: SWP Table A = 4,172,786 af/yr.;
SWP High Outflow Scenario – No BDCP = 1,870,000 af/yr.; With BDCP = 2,600,000 af/yr. [SWP/CVP deliveries = 4.705 maf/yr.]
SWP Low Outflow Scenario – No BDCP = ________ af/yr.; With BDCP = 3,320,000 af/yr. [SWP/CVP deliveries = 5.591 maf/yr.]
MWD Table A = 1,911,500 af/yr. (45.81%)
MWD High Outflow Scenario – With BDCP = 1.08 maf/yr. (Table A = 1.01 maf; Art. 21 = 0.03 maf; Art. 56 = 0.04 maf)
MWD Low Outflow Scenario – With BDCP = 1.40 maf/yr. (Table A = 1.29 maf; Art. 21 = 0.03 maf; Art. 56 = 0.08 maf)
MWD High Outflow Scenario – w/out BDCP = 0.81 maf/yr. (Table A = 0.80 maf; Art. 21 = 0.00 maf; Art. 56 = 0.01 maf)
MWD Low Outflow Scenario – w/out BDCP = 0.97 maf/yr. (Table A = 0.94 maf; Art. 21 = 0.00 maf; Art. 56 = 0.02 maf)
MWD HOS Incremental – (1.40 maf – 0.97 maf) = 0.43 maf/yr.
MWD LOS Incremental – (1.08 maf – 0.80 maf) = 0.28 maf/yr.
CALSIM (1922-2002) Table A Table ‘A’ Avg. Deliveries Article 21 Avg. Deliveries Table ‘A’ Incremental Article 21 Incremental
  SWP 100% 2,096,700 af/yr. 25,600 af/yr. _______ af/yr. _______ af/yr.
  MWD (100%) 45.8% 960,500 af/yr. 5,400 af/yr. 431,000 af/yr. 67,000 af/yr.
  MWD (110%) 50.4% 960,500 af/yr. 5,400 af/yr. 474,000 af/yr. 74,000 af/yr.
MWD‘s Long-Term Budget Forecasts assumed 50% SWP allocation to MWD (equivalent to a 110% BDCP participation level)
DWR SWP Delivery Reliability Report table:
The dry year supply from SWP is 430 TAF. Dry year is roughly a 10 percentile.
2005 Study – MWD Avg. = 1,418,747 AF/yr (68%); MWD Dry = 430,000 (10 %)
____________________________________________ From: Chan,Grace L Sent: Wednesday, April 30, 2014 5:16 PM To: Upadhyay,Devendra N Subject: SWP minimum delivery from reliability report
Deven, The table below shows the delivery from DWR SWP Delivery Reliability Reports over the years. The 2010 IRP was based on the draft 2011 report, so the current condition would be a minimum delivery of 9%. However, when we revert to 2005 reliability profile after Delta improvement the minimum was lowered. The reasoning is that with higher annual delivery, you may have a lower starting reservoir level when you get into drought and result with a lower minimum delivery. DWR stated that the 2013 and 2011 study are actually comparable. DWR’s explanation of higher delivery numbers because all contractors have requested their maximum Table A amount and higher demands mean higher maximum delivery. However, the minimum delivery also increased and DWR attributed that to model refinements.
SWP Reliability Report Table A Delivery |  |  | 
(% of Demand under then existing condition) |  |  | 
Report | Avg. | Min. | Max.
2005 Study | 68% | 4% | 93%
2007 Study | 63% | 6% | 90%
2009 Study | 60% | 7% | 81%
2011 Study | 61% | 9% | 82%
2013 Study | 62% | 12% | 97%

## Slide 100: State Water Project Cost Allocation Consensus Principles
New conveyance has definable benefits
Participants have proportional share in tunnel capacity
Available capacity/supply due to participation level can be purchased by other agencies on an at-cost basis
Contract model assumes high level of participation
100

## Slide 101: Financial Analysis

## Slide 102: Cost Allocation Funding Agencies
Ecosystem Restoration
Conveyance & Mitigation
Federal Government
State of California
CVP/SWP Contractors
Ag
Urban
Exchange
Refuge
Settlement
Ag
Urban
CVP Contractors
SWP Contractors

## Slide 103: Central Valley Project/State Water Project Long-Term Average Exports
Chart: 
| No Action Alternative | Alt 4 Low Outflow Scenario | Alt 4 High Outflow Scenario
Export SWP | 0.54 | 0.56 | 0.52
Export CVP | 0.46 | 0.44 | 0.48
CVP
CVP
CVP
SWP
SWP
SWP
Notes: Points
These splits are based on water supply delivered
Used as basis for initial discussions
CVP Deliveries
Exchange CVP Contractors 19.0%
South of Delta 16.8%
Refuge 5.2%
Total 40%

## Slide 104: Estimated Cost and Cost per Acre Foot Analysis

## Slide 105: California WaterFix Cost Allocation Analysis
 | 50% SWP Share | 55% SWP Share | 60% SWP Share
Financial Assumptions |  |  | 
Capital | $14.99 billion | $14.99 billion | $14.99 billion
O&M (over repay period) | $1.20 billion | $1.20 billion | $1.20 billion
SWP/CVP Cost Share | 50% / 50% | 55% / 45% | 60% / 40%
Contractor Share (MWD) | 45.81 % | 45.81 % | 45.81 %
Bond Rate | 6.135% | 6.135% | 6.135%
Discount-Inflation Rate | 0.0% | 0.0% | 0.0%
Repayment Period | 40 yrs. | 40 yrs. | 40 yrs.
MWD Annual Sales | 1.75 million | 1.75 million | 1.75 million
Cal WaterFix Alternative 4A (Year 2025) |  |  | 
SWP/CVP without Fix (2025) | 3.5 maf | 3.5 maf | 3.5 maf
SWP/CVP with Fix (2025) | 4.9 maf | 4.9 maf | 4.9 maf
SWP/CVP Restored Supplies | 1.4 maf | 1.4 maf | 1.4 maf
SWP Restored Supplies | 0.700 maf | 0.770 maf | 0.840 maf
MWD Restored Supplies | 0.321 maf | 0.353 maf | 0.385 maf
MWD Total Capital Cost | $3.43 billion | $3.78 billion | $4.13 billion
MWD Annual Debt Service Cost | $251 million | $276 million | $301 million
Melded Capital/O&M (at Delta) | $223 /AF | $223 /AF | $223 /AF
Melded Capital/O&M (at MWD) | $454 /AF | $454 /AF | $454 /AF
Incremental Capital/O&M (at Delta) | $782 /AF | $782 /AF | $782 /AF
Incremental Capital/O&M (at MWD) | $1,013 /AF | $1,013 /AF | $1,013 /AF
MWD T1 Treated w-WaterFix | $1,085 /AF | $1,100 /AF | $1,114 /AF
* The “at MWD” costs include California Aqueduct Power Cost ($200/AF) and WQ Treatment ($31/AF)
Notes: California Aqueduct Power Cost ($200/AF) and WQ Treatment ($31/AF)
1% drop in interest rate = $100 drop in Incremental Cost
MWD 2015 Tier 1 Treated Rate (without Cal Water Fix) = $942/AF
Water supply based on DWR CALSIM modeling of average Table A & incremental Cal Water Fix allocations
2015 MWD Tier 1 Treated Rate (without Cal WaterFix) = $942/AF
2015 MWD Tier 1 Treated Rate (with Cal WaterFix) = $942/AF Existing + ($300 M/1.75 million AF sales)

## Slide 106: Financing Costs - Cal WaterFix $15 Billion Capital Cost - 40 Year Term
Interest Rate | Annual Debt Service | Cost per Acre-foot (Based on 5 million af/yr.)
6.135% (So. Cal Water Comm.) | $ 1.0B/year | $200/af
5.0% | $874M/year | $175/af
3.7% (Current rates) | $732M/year | $146/af
2.62% (30-yr Treasury rate) | $610M/year | $122/af

## Slide 107: MWD Rates 2015
Full service – $942/af
Surcharges
  Treatment – $348/af
  Power – $138/af
  Stewardship – $41/af
  System Access – $259/af

## Slide 108: Permitting & Schedule

## Slide 109: California Water Fix Preliminary Draft Design and Construction Phases
Start
Year 16
Pump Plant
2.25 Years
4.5 Years
7.25 Years
Clifton Court
7 Years
10.75 Years
4 Years
4 Years
3 Years
IF
Intake
Tunnel
Site Work
Utilities
3 Years
IF
3 Years
Clifton Court
Tunnel
2.5 Years
Intake
2 Years
Pump Plant
3 Years
Utilities
Design Phase
Construction Phase
UNDER CONSTRUCTION
Simplifying with Planning, Start of Construction and End of Construction only

## Slide 110: Regulatory Trends

## Slide 111: Comparison of Regulatory Approaches
Consistent with past compliance approach for SWP/CVP ops
No regulatory or water supply assurances
No coverage for unlisted and CA fully protected species
Shorter duration for permits
No funding liability for public benefit conservation measures
Greater fishery agency control
New compliance approach for SWP/CVP operations
Regulatory and water supply assurances
Coverage for unlisted and CA fully protected species
Long-term permits (50 years)
Potential backstop of public funding shortfall
Greater opportunity for Contractor engagement
ESA Section 7 BO and CESA 2081 Permit
ESA Section 10 HCP and California NCCP

## Slide 112: Excess Storm Flow Analysis

## Slide 113: A modern system would allow storage of excess water for California
486,000 acre-feet
158 billion gallons
Enough for 3.6 million people for one year
Source: California WaterFix
Jan 1 – Mar 3
Notes: If we did have a modern fish friendly intake system then …

## Slide 114: With current facilities more runoff does not mean more supplies
January February March
Chart: Flow (cfs)
Storm #1 (21-day analysis)
1,622,000 AF Sacramento River
78,000 AF to State Water Project
SWP Pumping ~ 1,500 – 2,000 cfs
Sacramento River
Notes: The following two bar charts will illustrate the magnitude of outflows to exports and the amount of excess flow in the system
The blue line represents Sacramento River flow, not total inflow which includes the San Joaquin River and Eastside streams
The yellow dot represent actual delta smelt salvage: Jan 21 – 1 smelt caught at CVP Tracy; Feb 18 – 1 smelt caught at SWP Banks; Feb 22 – 1 smelt caught at CVP Tracy
Actual salvage x 4 = recorded salvage (Why? Only monitor 15 min/hr)
Delta outflow standard -- 6,000 cfs thru Jan; 11,000 cfs starting Feb
CVP was pumping about the same as the SWP
Storm #1 (Jan. 17 – Feb. 6; 21 days)
1,622,000 acre-ft. – Delta Outflow
78,000 acre-ft. – SWP (4.8%)
91,000 acre-ft. – CVP (5.6%)
Restrictions during winter storms resulted in 180,000 – 200,000 acre-ft lost to State Project, “January flows topped 50,000 cubic feet per second and peaked again in mid-February above 42,000 cubic feet per second. But rather than pumping as much water as possible under the biological opinions, pumping levels were ratcheted down for an entire month between mid-January and mid-February.
Delta smelt take threshold for 2016 = 14 actual fish salvaged or 56 expanded based on the 15 min/hr monitoring (the lowest ever)
Delta smelt caught = 3 fish or 12 expanded (20% of incidental take limit)
Currently, the incidental take level for all listed species is very low. For adult Delta smelt we are at approximately 20% of the ITL. For winter run we are approximately 1% of the ITL. For unclipped steelhead we are approximately 2.6% of the ITL. The incidental take level is the take by the Projects anticipated by the fish agencies for operations conducted pursuant to the reasonable and prudent alternatives. Currents numbers are well below what the agencies anticipated would be taken, and therefore provide room for experimentation.
“Any level of salvage observed at either (pumping) facility will be of concern,” the Delta Smelt Working Group said in its weekly report. (Jan. 11)
Jan. 11 -- Though neither the hard turbidity trigger (12NTU at PPT, HOL and VCU), nor the hard salvage trigger (3 days of salvage of Delta Smelt) has been met, the DWR turbidity transect survey and FWS early warning survey indicate that fish movement has occurred, and entrainment protection actions consistent with the intent of Action 1 are needed to protect pre-spawning Delta Smelt adults.
Delta fish monitoring
CDFW has released the 2015 FMWT indices:
The 2015 Delta Smelt annual FMWT index is 7.
The 2015 Longfin Smelt annual FMWT index is 4.
Both indices are the lowest on record (i.e. since 1967).
The take home: Incidental take is set at 1,017 and 1,554 natural and hatchery produced juveniles, respectively.
The BiOp calls for take to be set at 2% of the Juvenile Production Estimate (JPE), but in practice has been set at 1% of JPE with a 50% allowance to account for run-type misidentification due to use of the length-at-date criteria. New this year is a genetic determination program to eliminate the uncertainty of run-type identification. This year’s take is 1% of JPE (no more 50% allowance) of the Juvenile Production Estimate for naturally produced fish and 1% of hatchery produced fish. This take is lower numerically than the past two years (2013: 23,928 natural, 309 hatchery; 2014: 2,490 natural, 1,885 hatchery). However, past year’s actual take has been only 1-10% of the ITL. Therefore, barring unforeseen conditions I would not expect the winter-run ITL to be met/exceeded this year. NMFS estimates a JPE of 101,716 natural-origin juvenile winter-run entering the Delta during water year 2016 (enclosure 3). Based upon CDFW historical monitoring data at Knights Landing rotary screw traps, winter-run juveniles are expected to emigrate into the Delta from November 2015 to April 2016. In early February 2016, approximately 420,000 winter-run juveniles propagated at LSNFH will also be released into the upper Sacramento River near Redding.

## Slide 115: With current facilities more runoff does not mean more supplies
Chart: Flow (cfs)
| 42434 | 42435 | 42436 | 42437 | 42438 | 42439 | 42440 | 42441 | 42442 | 42443 | 42444 | 42445 | 42446 | 42447 | 42448 | 42449 | 42450 | 42451 | 42452 | 42453 | 42454
Sacramento River @ Freeport (cfs) | 13971 | 16068 | 22154 | 39918 | 52705 | 59421 | 60560 | 61012 | 65366 | 71899 | 76108 | 76760 | 75887
SWP Pumps (cfs) | 2315 | 2211 | 1915 | 2416 | 2402 | 1552 | 3485 | 2988 | 3087 | 2936 | 2890 | 3269 | 3699 | 4528
Sacramento River Forecast (cfs) | 75887 | 75000 | 74000 | 73000 | 71000 | 69000 | 68000 | 65000 | 60000 | 58000
SWP Forecast (cfs) | 4528 | 4000 | 4000 | 3500 | 3500 | 3000 | 3000 | 3000 | 3000
Sac River + Yolo Bypass | 16370 | 24369 | 42984 | 53490 | 59867 | 62237 | 65081 | 77009 | 109970 | 134117 | 140306 | 129923
Storm #2 (21-day analysis)
~ 2.4 million AF Sacramento River
~ 2.9 million AF Sacramento River + Bypass
~ 0.12 million AF to State Water Project
SWP Pumping ~ 2,000 to 3,700 cfs
March
Sac River +
Yolo Bypass
Sacramento River
Notes: Storm #2 (Mar 4 – Mar 24; 21 days)
2.9 million acre-ft. – Sac River + Yolo Bypass
120,000 acre-ft. – SWP (4.6%)
xx,000 acre-ft. – CVP (___%)
Delta smelt take threshold for 2016 = 14 actual fish salvaged or 56 expanded based on the 15 min/hr monitoring (the lowest ever)
Delta smelt caught = 3 fish or 12 expanded (20% of incidental take limit)
Currently, the incidental take level for all listed species is very low. For adult Delta smelt we are at approximately 20% of the ITL. For winter run we are approximately 1% of the ITL. For unclipped steelhead we are approximately 2.6% of the ITL. The incidental take level is the take by the Projects anticipated by the fish agencies for operations conducted pursuant to the reasonable and prudent alternatives. Currents numbers are well below what the agencies anticipated would be taken, and therefore provide room for experimentation.
“Any level of salvage observed at either (pumping) facility will be of concern,” the Delta Smelt Working Group said in its weekly report. (Jan. 11)
Jan. 11 -- Though neither the hard turbidity trigger (12NTU at PPT, HOL and VCU), nor the hard salvage trigger (3 days of salvage of Delta Smelt) has been met, the DWR turbidity transect survey and FWS early warning survey indicate that fish movement has occurred, and entrainment protection actions consistent with the intent of Action 1 are needed to protect pre-spawning Delta Smelt adults.
Delta fish monitoring
CDFW has released the 2015 FMWT indices:
The 2015 Delta Smelt annual FMWT index is 7.
The 2015 Longfin Smelt annual FMWT index is 4.
Both indices are the lowest on record (i.e. since 1967).
The take home: Incidental take is set at 1,017 and 1,554 natural and hatchery produced juveniles, respectively.
The BiOp calls for take to be set at 2% of the Juvenile Production Estimate (JPE), but in practice has been set at 1% of JPE with a 50% allowance to account for run-type misidentification due to use of the length-at-date criteria. New this year is a genetic determination program to eliminate the uncertainty of run-type identification. This year’s take is 1% of JPE (no more 50% allowance) of the Juvenile Production Estimate for naturally produced fish and 1% of hatchery produced fish. This take is lower numerically than the past two years (2013: 23,928 natural, 309 hatchery; 2014: 2,490 natural, 1,885 hatchery). However, past year’s actual take has been only 1-10% of the ITL. Therefore, barring unforeseen conditions I would not expect the winter-run ITL to be met/exceeded this year.
NMFS estimates a JPE of 101,716 natural-origin juvenile winter-run entering the Delta during water year 2016 (enclosure 3). Based upon CDFW historical monitoring data at Knights Landing rotary screw traps, winter-run juveniles are expected to emigrate into the Delta from November 2015 to April 2016.
In early February 2016, approximately 420,000 winter-run juveniles propagated at LSNFH will also be released into the upper Sacramento River near Redding.

## Slide 116: Excess Storm Flows – WY 2009-2010 Reoperation Analysis with BDCP Cal Water Fix Alt. 4A
Chart: Flow (cfs)
Water Year | Year Type | Excess Flow Period | Reoperation Benefit
2009-2010 | Below Normal | 1/20/2010 - 3/16/2010 | 450,000 AF

## Slide 117: Excess Storm Flows – WY 2010-2011 Reoperation Analysis with BDCP Cal Water Fix Alt. 4A
Chart: Flow (cfs)
Water Year | Year Type | Excess Flow Period | Reoperation Benefit
2010-2011 | Wet | 12/07/2010 -7/11/2011 | 2,530,000 AF

## Slide 118: Water Quality Analysis

## Slide 119
California WaterFix
Improves Water Quality
27% salinity reduction
Colorado River
650 mg/l
Sacramento River
100 mg/l
SWP (Existing)
302 mg/l
SWP (Cal Water Fix) 221 mg/l
(27% improvement)
San Joaquin River
320 mg/l
Sacramento, San Joaquin & Colorado River water quality represents historical average annual recorded data
State Water Project water quality is a comparison of modeled data from the Recirculated Draft EIR/EIS
Notes: Recirculated Draft EIR/S Water Quality Modeling Results
Average Salinity at Banks PP for Alternative 4A
Existing Conditions (EC, µmhos/cm) Alternative 4A (EC, µmhos/cm) % Improvement
All Water years 530 388 27%
Drought conditions 646 491 24%
119

## Slide 120
Colorado River
0.06 mg/l
Sacramento River
0.02 mg/l
SWP (Existing)
0.36 mg/l
SWP (Cal Water Fix) 0.22 mg/l
(37% improvement)
Sacramento, San Joaquin & Colorado River water quality represents historical average annual recorded data
State Water Project water quality is a comparison of modeled data from the Recirculated Draft EIR/EIS
San Joaquin River
0.1 – 0.4 mg/l
California WaterFix
Improves Water Quality
37% bromide reduction
Notes: Source: Appendix B. Supplemental Modeling Results for New Alternatives, Table EC-2.
RDEIR/S Water Quality Modeling Results
Average Bromide at Banks PP for Alternative 4A
Existing Conditions (µg/L) Alternative 4A (µg/L) % Improvement
All Water years 356 224 37%
Drought conditions 469 319 32%
Source: Appendix B. Supplemental Modeling Results for New Alternatives, Table Br-2.
Notes:
The data in these tables are summarized modeling results from the water quality modeling studies conducted to evaluate water quality effects of the BDCP/California Water Fix. The average concentrations are modeling results and are not actual conditions. Focus on the percent reduction as more informative.
Sacramento River at Greene’s Landing 0.018 mg/L average annual historical sampled data
Bromide at the Banks Pumping Plant has averaged 0.230 mg/L in recent years (1990-2006). -- http://www.waterboards.ca.gov/rwqcb5/water_issues/drinking_water_policy/salinity_conceptual_model/pgs13_27.pdf
120

## Slide 121: California WaterFix is important for groundwater storage
Bay Delta provides high quality water
Essential to reduce salt impacts
Critical for groundwater storage
Orange
County
Main
San Gabriel
Raymond
Chino
San Jacinto
Las Posas
Cuchamonga
Warner Valley
Elsinore
Upper San Juan
San Mateo & San Onofre
Six Basins
Sylmar
Verdugo
East San
Fernando
121
Notes: Supply Salt (TDS mg/l) Salt (Lbs / acre ft)
Colorado River ~ 500 to 700 mg/l 1,360 to 1,900 lbs/af
Bay Delta (current) ~ 300 mg/l 700 lbs/af
Bay Delta (new conveyance) ~ 200 mg/l 470 lbs/af
Objectives
Improve export quality to meet Public Health standards & reduce treatment costs
Support actions to minimize salinity imports
Meet 500 mg/l blending goal
Some Basin Plans have low TDS objectives that could restrict extended recharge of high salinity Colorado River water *
Salinity Management Policy (Board Policy March 1999)
Protect imported quality and seek salinity reductions
Establish total dissolved solids objective of < 500 (mg/L)
Optimize the long-term use of Colorado River water in conjunction with State Water Project supplies
Make the Salinity Management Action Plan the primary strategy to carry out this policy
Support actions to minimize salinity imports to enhance groundwater and recycled water programs
Regional Board Basin Plans have TDS water quality objectives for groundwater. Raymond and Main San Gabriel Basins objectives are at 450 mg/L TDS, the eastern portions of San Fernando Basin range from 400 to 600 mg/L. Some parts of Chino Basin have TDS objectives in the 200-300 mg/L range. Central Basin is higher at 700 mg/L. Orange Co Basin is 580 mg/L.

## Slide 122
State Project Water
Colorado
Water
Blend ing
Zone
MWD SWP Supplies | Blending
Existing (Avg. Yr.) | Met
BDCP Preferred Alt | Met
Delta No Fix (Avg. Yr.) | Sometimes
Delta No Fix (Below Normal) | Rarely
Blending
Zone
California WaterFix allows MWD blending goals to be met
Notes: Metropolitan’s SWP Supplies Supplies Blending
Existing 1,200,000 AFY Met
BDCP Preferred Alt. 1.2 – 1,400,000 AFY Met
Delta No Fix (Avg Yr) 875,000 AFY Sometimes
Delta No Fix (Below Normal) ~675,000 AFY Rarely
Blending Target Requirements
~50% SWP Allocation to meet blend targets 950,000 AFY
~35% SWP Table A to cover Exclusive Zones 665,000 AFY
ASSUMPTIONS
• BDCP no fix scenario = 3.5 maf/yr SWP/CVP; MWD is 1/4 or 850,000 af/year ON AVERAGE - LONG-TERM!!!!!
• 850,000 AF to MWD represents 44.5% of SWP Table A (i.e. this is the new long-term baseline)
• No SWP banking and suface water accounts to use for blending (i.e. only for reliability)
• Reliability is number 1 priority; Blending and meeting TDS targets is a secondary priority
• MWD needs a 50% SWP allocation needed to meet blend targets; or 1.9 maf x 50% = 950,000 AF
• MWD needs about 35% to cover exclusives, then we can blend (or 35% x 1.9 maf = 665,000 AF/yr)
• MWD needs 16% allocations (or 300,000 AF) to meet blending goals
• SWP minimum to consider starting to blend = 37% allocation or 707,000 AF
• Runoff indexes -- Critical, Dry, Below Normal, Above Normal, Wet
• Runoff indexes = Critical-16%, Dry-16%, BN-16%, AN-15%, Wet-35% (based on historical Sac 4-River Runoff Index)
THEREFORE
• Unless runoff is above average, you cannot meet blending needs.
DEVELOP CHARTS & MEMBER AGENCY PERCENTAGE MATRICES
• Scenario 1: Existing SWP/CVP Supplies (4.7 MAF/4 = 1.2 MAF on average) -- Blending goals met, show CRA area, SWP area, blending area
• Scenario 2: BDCP No Fix with Avg Yr runoff (3.5 MAF/4 = 850 TAF or 1.7 maf minus 50%) -- 100% of the time you will not need meet blending goals (i.e. only partial blending allowed in a smaller portion of MWD service area)
• Scenario3: BDCP No Fix with Below Normal Yr runoff (665 TAF or 1.7) -- 22% of time you cannot do any blending [(850,000-665,000)/850,000 = 22%; assumes linear relationship with runoff index]
MWD Water Quality Treatment Plants
Normal operating conditions (Nov 04-Oct 13) (Average) SWP CRA
Jensen 100% 0%
Weymouth 41% 59%
Diemer 39% 61%
Mills 100% 0%
Skinner 39% 61%

## Slide 123: 3,000 vs 6,000 cfs Capacity Analysis

## Slide 124: 3,000 vs. 9,000 cfs Conveyance Preliminary Estimate of MWD’s Cost Share Capital Cost Estimate
Chart: Capital Cost Estimates ($ Billions)
3,000 cfs | 8.9
9,000 cfs | 14.9
3000 cfs – Assumes no participation/cost share from CVP Ag, SWP Ag, & Feather River urban
3,000 cfs
9,000 cfs
MWD Share ~ $5.7 billion
MWD Share ~ $3.8 billion
Checking--Update
Notes: Cost estimates (from BDCP)
9,000 cfs – 14.9 billion
3,000 cfs – 8.9 billion
SWP Table A
Urban Contractors (w/o Feather River Urban) – 2.98 million AF
Ag Contractors – 1.15 million AF
Total (w/o Feather River Urban) – 4.13 million AF
MWD Share
3,000 cfs – Assumes no CVP, no SWP Ag, no Feather River urban; Therefore, MWD’s share(1.911 maf)/Total Urban share(2.98 maf) = 64%, or 1,920 cfs; 64% of $8.9 billion = $5.7 billion
9,000 cfs – Assumes SWP/CVP cost split of 55%/45%. MWD’s share (1.911 maf)/Total SWP w-o Feather River share (4.13 maf) = 46%. Therefore, $14.9 billion x 55% x 46% = $3.77 billion, or 25%; Capacity share 25% of 9,000 cfs = 2,250 cfs

## Slide 125: 3,000 cfs Conveyance with 32’ID Single Main Tunnel
Features | Feature Costs (With PM/CM/Eng and Contingency)
Intakes | $ 303,600,000
Conveyance | $ 82,761,360
Pumping Plants | $ 274,697,280
Forebays | $ 581,856,000
Tunnels | $ 6,581,929,024
Roads | $ 382,158,082
Utilities and Communication | $ 192,295,676
Subtotal | $ 8,399,297,422
Land and Rights | $ 150,000,000
Construction Related Mitigation | $ 330,000,000
Grand Total | $ 8,879,297,422

## Slide 126: 9,000 cfs Conveyance with 40’ID Dual Main Tunnels
Summary | Feature Costs (With PM/CM/Eng and Contingency)
Intakes | $ 597,168,000
Conveyance | $ 249,585,600
Pumping Plants | $ 687,508,800
Forebays | $ 581,856,000
Tunnels | $ 11,718,781,402
Roads | $ 382,158,082
Utilities and Communication | $ 192,295,676
Subtotal | $ 14,409,353,560
Land and Rights | $ 150,000,000
Construction Related Mitigation | $ 330,000,000
Grand Total | $ 14,889,353,560

## Slide 127: Collaborative Science & Adaptive Management

## Slide 128
Bay Delta Conservation Plan
Collaborative Science & Adaptive Management
Ongoing Collaborative Science
  Two-tiered collaborate policy & technical team
  Conducts joint research on key Delta fishery issues
  Includes
    United States Fish and Wildlife Service
    National Marine Fisheries Service
    California Department of Fish and Wildlife
    United States Bureau of Reclamation
    California Department of Water Resources
    Environmental interests (NRDC, TNC, PCFFA and Water4Fish)
    Non-Governmental Organizations
    State and Federal water contractors
Notes: General Background
The CSAMP was launched following a decision by the United States District Court for the Eastern
District of California on April 9, 2013 entitled “Memorandum Decision and Order regarding
Motion to Extend Remand Schedule” (“Court Order”), issued in response to a motion to extend
the court3ordered remand schedule for completing revisions to salmon (NMFS 2009) and Delta
Smelt (FWS 2008) Biological Opinions (“BiOps”).
CSAMP Policy Group
Jim Beck…….……………………………………….…………... Kern County Water Agency
Thomas Birmingham……………………………………….. Westlands Water District
Charlton “Chuck” Bonham….……………………….….. CA Department of Fish and Wildlife
Mark Cowin………………….…………………………………. CA Department of Water Resources
Zeke Grader…………………………………………………….. Golden Gate Salmon Association
Ren Lohoefener………………………………………………. U.S. Fish and Wildlife Service
Jeff Kightlinger..………………………………………………. Metropolitan Water District of Southern California
David Murillo…………………………………………………… U.S. Bureau of Reclamation
Bill Phillimore………………………………………………….. Coalition for a Sustainable Delta
Dick Pool…………...……………………………………………. Water4Fish
Kate Poole……….................................................... Natural Resources Defense Council
William Stelle....................................................... National Marine Fisheries Service
Jay Ziegler…..…………............................................. The Nature Conservancy
Collaborative Adaptive Management Team (CAMT)
Gary Bobker………………………………………………….... The Bay Institute
Frances Brewster…………………………………………….. Santa Clara Valley Water District
Mike Chotkowski…………………………………………….. U.S. Fish and Wildlife Service
Valerie Connor, Co-Chair…………………………………. State and Federal Contractors Water Agency
Sue Fry…………………………………………………………….. U.S. Bureau of Reclamation
Lauren Hastings………………………………………………. Delta Science Program
Steve Lindley…………………………………………………… National Marine Fisheries Service
Laura King Moon.................................................. CA Department of Water Resources
Anke Mueller-Solger............................................ Interagency Ecological Program
Maria Rea............................................................. National Marine Fisheries Service
Carl Wilcox........................................................... CA Department of Fish and Wildlife
Leo Winternitz, Co-Chair...................................... The Nature Conservancy

## Slide 129
Bay Delta Conservation Plan
Collaborative Science & Adaptive Management
Adaptive Management & Monitoring Plan
  Mechanism to review and appropriately adjust existing and new operating requirements based on new scientific information and monitoring
  Addresses gaps in knowledge
  Demonstrate project avoids jeopardy to listed species
Notes: General Background
The CSAMP was launched following a decision by the United States District Court for the Eastern
District of California on April 9, 2013 entitled “Memorandum Decision and Order regarding
Motion to Extend Remand Schedule” (“Court Order”), issued in response to a motion to extend
the court3ordered remand schedule for completing revisions to salmon (NMFS 2009) and Delta
Smelt (FWS 2008) Biological Opinions (“BiOps”).
CSAMP Policy Group
Jim Beck…….……………………………………….…………... Kern County Water Agency
Thomas Birmingham……………………………………….. Westlands Water District
Charlton “Chuck” Bonham….……………………….….. CA Department of Fish and Wildlife
Mark Cowin………………….…………………………………. CA Department of Water Resources
Zeke Grader…………………………………………………….. Golden Gate Salmon Association
Ren Lohoefener………………………………………………. U.S. Fish and Wildlife Service
Jeff Kightlinger..………………………………………………. Metropolitan Water District of Southern California
David Murillo…………………………………………………… U.S. Bureau of Reclamation
Bill Phillimore………………………………………………….. Coalition for a Sustainable Delta
Dick Pool…………...……………………………………………. Water4Fish
Kate Poole……….................................................... Natural Resources Defense Council
William Stelle....................................................... National Marine Fisheries Service
Jay Ziegler…..…………............................................. The Nature Conservancy
Collaborative Adaptive Management Team (CAMT)
Gary Bobker………………………………………………….... The Bay Institute
Frances Brewster…………………………………………….. Santa Clara Valley Water District
Mike Chotkowski…………………………………………….. U.S. Fish and Wildlife Service
Valerie Connor, Co-Chair…………………………………. State and Federal Contractors Water Agency
Sue Fry…………………………………………………………….. U.S. Bureau of Reclamation
Lauren Hastings………………………………………………. Delta Science Program
Steve Lindley…………………………………………………… National Marine Fisheries Service
Laura King Moon.................................................. CA Department of Water Resources
Anke Mueller-Solger............................................ Interagency Ecological Program
Maria Rea............................................................. National Marine Fisheries Service
Carl Wilcox........................................................... CA Department of Fish and Wildlife
Leo Winternitz, Co-Chair...................................... The Nature Conservancy

## Slide 130: Emergency Preparedness

## Slide 131: Tactical Coordination
Unified command integrates Cal OES, DWR, USACE and local operations
MOA between DWR and USACE
DWR’s model estimates time & cost of repairs
Emergency plans are tested under simulated floods and earthquakes
On-call contracts for materials
Notes: Unified command integrates Cal OES, DWR, USACE and local operations
MOA between DWR and USACE coordinates tactical response
Pre-defined missions framework are flexible and scalable
DWR’s tactical model predicts time and cost of repairs
Emergency plans are tested under simulated floods and earthquakes
IDIQ and On-call contracts for materials, response and repair

## Slide 132
I-5
Stockton Loading & Stockpile Site
Notes: 3 Proposed Emergency Stockpile Sites
Stockton – DW Ship Channel/Interstate 5
Brandon Island – Southern tip
Rio Vista – Current Stockpile Area

## Slide 133: Climate Change Analysis

## Slide 134: Climate Change Analysis Overview
Summary
  Cal Water Fix analysis & design incorporates climate change
  Cal Water Fix provides climate change adaptation
Analyses
  Effects on water quality & water supply (DWR analysis)
  Effects on North Delta intake location (CH2M analysis)
Assumptions
  20 global climate models used to project Delta sea-level rise
  Time periods modeled – 2025, 2060, 2100

## Slide 135
Preliminary Subject to Revision
Tunnels
SJ River
Through Delta
CVP Pumps
SWP Pumps
Sacramento
Stockton
Sac River
West Canal
East Canal
Climate Change Analysis
Effects on Delta Intake Location
SWP Pumps
CVP Pumps
South Delta
Existing forebay expansion
Consolidated pumping facility
Use of State-owned land
Central Delta
2 gravity-flow tunnels (30 miles long; 9,000 cfs)
North Delta
3 river intakes
Modern fish screens
28-acre forebay
Sea Level Rise Effects with Cal Water Fix
(On Average)
2015
2025
2060
2100
Salinity lines indicate 2,000 ppm TDS
Analysis conducted by CH2M for Metropolitan Water District
Salinity lines indicate 2,000 ppm TDS
135
Notes: 135
Sea Level Rise
– Year 2025, 15 cm, 5.9 inches
– Year 2060, 45 cm, 17.7 inches
– Year 2100, 140 cm, 55.1 inches
Analysis by CH2M (10-04-2013)
– Assumes BDCP operations
– 50 percentile with BDCP Operations
– 0 inches, X2 = 80.3 km
– 6 inches, X2 = 80.8 km
– 18 inches, X2 = 80.6 km
– 55 inches, X2 = 87.6 km
– 75 percentile with BDCP Operations
– 0 inches, X2 = 85.9 km
– 6 inches, X2 = 86.6 km
– 18 inches, X2 = 86.5 km
– 55 inches, X2 = 92.5 km
– 90 percentile with BDCP Operations
– 0 inches, X2 = 91.8 km
– 6 inches, X2 = 92.6 km
– 18 inches, X2 = 91.9 km
– 55 inches, X2 = 96.2 km
– October 1977 with BDCP Operations
– 0 inches, X2 = 94.1 km
– 6 inches, X2 = 95.1 km
– 18 inches, X2 = 94.4 km
– 55 inches, X2 = 101.3 km
Location Map
– Golden Gate Bridge = 0 km
– Chipps Island = 75 km
– Collinsville = 81 km
– Emmaton = 92 km
X2 Position can be controlled even at 140cm (55”) sea level rise, but with significant water cost (1 MAF)
Due to increase in export in Preferred Project salinity in the South Delta increases

## Slide 136
Preliminary Subject to Revision
Tunnels
SJ River
Through Delta
CVP Pumps
SWP Pumps
Sacramento
Stockton
Sac River
West Canal
East Canal
Climate Change Analysis
Effects on Delta Intake Location
SWP Pumps
CVP Pumps
South Delta
Existing forebay expansion
Consolidated pumping facility
Use of State-owned land
Central Delta
2 gravity-flow tunnels (30 miles long; 9,000 cfs)
North Delta
3 river intakes
Modern fish screens
28-acre forebay
Sea Level Rise Effects with Cal Water Fix
(Drought Conditions)
Salinity lines indicate 2,000 ppm TDS
Analysis conducted by CH2M for Metropolitan Water District
2015
2025
5.9”
2060
17.7”
2100
55.1”
136
Notes: 136
Sea Level Rise
– Year 2025, 15 cm, 5.9 inches
– Year 2060, 45 cm, 17.7 inches
– Year 2100, 140 cm, 55.1 inches
Analysis by CH2M (10-04-2013)
– Assumes BDCP operations
– 50 percentile with BDCP Operations
– 0 inches, X2 = 80.3 km
– 6 inches, X2 = 80.8 km
– 18 inches, X2 = 80.6 km
– 55 inches, X2 = 87.6 km
– 75 percentile with BDCP Operations
– 0 inches, X2 = 85.9 km
– 6 inches, X2 = 86.6 km
– 18 inches, X2 = 86.5 km
– 55 inches, X2 = 92.5 km
– 90 percentile with BDCP Operations
– 0 inches, X2 = 91.8 km
– 6 inches, X2 = 92.6 km
– 18 inches, X2 = 91.9 km
– 55 inches, X2 = 96.2 km
– October 1977 with BDCP Operations
– 0 inches, X2 = 94.1 km
– 6 inches, X2 = 95.1 km
– 18 inches, X2 = 94.4 km
– 55 inches, X2 = 101.3 km
Location Map
– Golden Gate Bridge = 0 km
– Chipps Island = 75 km
– Collinsville = 81 km
– Emmaton = 92 km
X2 Position can be controlled even at 140cm (55”) sea level rise, but with significant water cost (1 MAF)
Due to increase in export in Preferred Project salinity in the South Delta increases

## Slide 137: Climate Change Analysis Effects on Delta Intake Location
South Intake | 2010 | 2025 | 2060
Salinity (TDS mg/L) | 301 | 311 | 326
Bromide (mg/L) | 0.34 | 0.35 | 0.35
North Intake | 2010 | 2025 | 2060
Salinity (TDS mg/L) | 111 | 111 | 111
Bromide (mg/L) | 0.08 | 0.08 | 0.08
Combined | 2010 | 2025 | 2060
Salinity (TDS mg/L) | 214 | 221 | 228
Bromide (mg/L) | 0.21 | 0.22 | 0.22
Based on BDCP Draft EIR/S Alternative 4-H4
Analysis conducted in 2013 by CH2M for Metropolitan Water District.

## Slide 138
Chart: Avg. SWP-CVP Exports (million AF)
| 2015 Operations | 2025 Operations | 2060 Operations
Without – Cal Water Fix | 4.9 | 4.7 | 4.44
9,000 cfs Facility
With – Cal Water Fix | 5.3 | 5
Climate Change Analysis
Potential Impacts of Sea-Level Rise on SWP/CVP Exports
Information from DWR CALSim model; MWD share ~ 25%; 2060 operations are preliminary estimates
The “without” Cal Water Fix assumes no reduction in future supplies due to potential additional eco-restrictions
Without
Cal Water Fix
Without
Cal Water Fix
With
Cal Water Fix
With
Cal Water Fix
Existing
Notes: The analysis assumes no California Water Fix (i.e. no northern Delta intake). The cause of the decreased SWP/CVP exports is due to the extra amount of outflow needed to maintain SWRCB standards and biological opinion flow requirements.
Climate Change Analysis
Potential Impacts of Sea-Level Rise on SWP/CVP Exports
Alternative 2015 2025 2060 2100
No CalWater Fix 4.9 maf 4.7 maf 4.4 maf 3.8 maf
With Cal Water Fix No model run 4.7 – 5.3 maf No model run No model run
With BDCP No model run 4.7 – 5.6 maf 4.4 – 5.3 maf No model run
4.7 – 5.3 maf/yr – NEW BDCP / Cal Water Fix Preferred Alternative (evaluated in Draft EIR/S as Alternative 4A H3-H4 at early long-term 2025)
4.7 – 5.6 maf/yr – PREVIOUS BDCP Preferred Alternative (evaluated in Draft EIR/S as Alternative 4 H1-H4 at late long-term 2060)

## Slide 139: Conveyance Alternatives Analyzed

## Slide 140: CALFED Alternatives
Transfer Supplies for the Drought Water Bank
Yolo Bypass Conveyance Facility
Habitat Restoration
Habitat Restoration w/ Dedicated Enviro Water
Extensive Habitat Restoration w/ New Storage
Water Management w/ Environmental Storage
Chain of Lakes Isolated Facility
Additional Export Capacity w/ South of Delta Storage
Delta Island Protection and Small Isolated Facility
Improved Thru-Delta Conveyance w/ Screened Diversion at Hood
Dual Transfer Facility
East-Side Foothill Large Conveyance Facility
West-Side Sacramento Small Transfer Facility
West-Side Sacramento Storage/ Conveyance Facility
East-Side Delta Isolated Facility
Protection of Delta Islands/ Functions
Delta Island Protection w/Storage
Pollutant Source Controls/ Operational Changes
Source Control/Added Storage

## Slide 141: Post CALFED Through-Delta Focus
Eco-Crescent Conveyance
CCWD – San Joaquin Intake
Russ Brown – Delta Corridors
Terry Spragg – Water Bags
Polder Concept – Joint Protection of Multiple Islands
Franks Tract Gates for Water Quality/Fish Avoidance
Two-Gates Fish Protection Project
In-Delta Gate Operations
Three-Mile Slough Gate
Central Delta Intake
Op Changes for Fish Protection
Georgiana Slough Gates
Sutter/Steamboat Barriers for Delta Freshwater Enhancement
Reoperation of Cross-Channel Gates
Multiple Intake for Fish Protection
South Delta Export Recirculation
Deep Water Ship Channel Intake
South Delta Fish Facilities Forum
In-Delta Storage
South Delta Operable Gates Study
Phase VIII Enhanced Flow Process
Tracy Fish Test Facility
Salinity Protection Barriers/Gates at Railroad Cut and Empire Cut
DWR Delta Emergency Preparedness and Response Plan
Stockton Dissolved Oxygen Study
Vernalis Adaptive Management Plan

## Slide 142: Initial Alternative Screening Reports
Conveyance Alternative – Dual Conveyance (A1-A4)
  Dual Conveyance – Tunnels to South Delta (3k – 15k cfs)
  Dual Conveyance – East Canal to South Delta (3k – 15k cfs)
  Dual Conveyance – West Canal to South Delta (3k – 15k cfs)
  Dual Conveyance – East Canal to San Joaquin R. (3k – 15k cfs)
Conveyance Alternative – Isolated Conveyance (B1-B7)
  North Delta Tunnel – Abandon South Delta Intakes (15k cfs)
  East Canal – Abandon South Delta Intakes (15k cfs)
  West Canal – Abandon South Delta Intakes (15k cfs)
  Feather River/Foothill Canal – Abandon So. Delta (15k cfs)
  Sac Ship Channel – Abandon South Delta Intakes (15k cfs)
  Fremont Weir Tunnel – Abandon South Delta Intakes (15k cfs)
  Antioch Tunnel w/Desal – Abandon South Delta Intakes (15k cfs)

## Slide 143: Initial Alternative Screening Reports
Conveyance Alternative – Through Delta (C1-C4)
  Through-Delta – Separate Corridors (15k cfs)
  Through-Delta– Armored Corridors (15k cfs)
  Through-Delta – Delta Salinity Barrier (15k cfs)
  Through-Delta – New Clifton Court Forebay Screens (15k cfs)

## Slide 144: Bay Delta Conservation Plan Summary of Alternatives Evaluated
BDCP Proposed Action (9,000 cfs tunnel)
West Canal (15,000 cfs)
Tunnels (3,000, 6,0000 and 15,000 cfs)
Isolated facility (15,000 cfs)
Through-Delta
Less Tidal Restoration
More Restoration
More Spring Outflow

## Slide 145: Additional Proposals
Delta
  Natural Resources Defense Council – Portfolio Proposal
  Robert Pyke – Western Delta Intakes Concept
  Peer Swan – An Alternative Vision
Statewide
  ACWA – Statewide Water Action Plan
  Delta Stewardship Council – Delta Plan
  Delta Vision Foundation Process
  Public Policy Institute of California – Comparing Futures for the Sacramento/San Joaquin Delta

## Slide 146: California EcoRestore

## Slide 147: California EcoRestore Projects Rough Cost Estimate
SWP/CVP Bio Op Mandates (25,000 acres)
  Floodplain Restoration (17,000 ac.) $719 M
  Tidal Habitat (8,000 ac.) $235 M
State Proposition 1 Grants (5,000 acres)
  Floodplain Restoration (500 ac.) $21 M
  Managed Wetlands (3,500 ac.) $40 M
  Tidal Habitat (1,000 ac.) $29 M
Add Assumptions
Notes: California EcoRestore is an initiative to help coordinate and advance at least 30,000 acres of critical habitat restoration in the Sacramento – San Joaquin Delta over the next four years. Driven by world-class science and guided by adaptive management, California EcoRestore will aggressively pursue habitat restoration projects with clearly defined goals, measurable objectives, and financial resources to help ensure success.
A broad range of habitat restoration projects will be pursued, including projects to address aquatic, sub-tidal, tidal, riparian, flood plain, and upland ecosystem needs.
California EcoRestore’s initial goal is to advance (i.e. complete or break ground on) 30,000 acres of Delta habitat restoration:
25,000 acres associated with existing mandates for habitat restoration, pursuant to federal biological opinions. These projects will be funded exclusively by the state and federal water contractors that benefit from the State Water Project and the Central Valley Project systems.
5,000 acres of habitat enhancements. Proposition 1 grants to local governments, non-profit organizations, and other entities will support these habitat enhancements throughout the Delta. Funding will come primarily from the Delta Conservancy, the California Department of Fish and Wildlife, and the California Department of Water Resources.
California EcoRestore is unassociated with any habitat restoration that may be required as part of the construction and operation of new Delta water conveyance (California WaterFix).
California EcoRestore Funding
Costs for California EcoRestore are expected to reach at least $300 million in the first four years. Much of these costs will be borne by the state and federal public water agencies currently required to mitigate the ecological impacts of the State Water Project and the Central Valley Project in the Delta.
Funding for habitat enhancements unassociated with mitigation will come primarily from Propositions 1 and 1E, the AB 32 Greenhouse Gas Reduction Fund, and local, federal, and private investment.
More information on California EcoRestore is available through the links below:
EcoRestore Fact Sheet http://resources.ca.gov/ecorestore/

## Slide 148: MWD water sales average 2.0 million ft.
Chart: Fiscal Year Ending
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
Actual Sales | 2427357 | 2071103.8 | 2110923.1 | 2349973.5 | 2256750.6 | 2151218.4 | 1767593.9 | 1602368.7 | 1698545.1 | 1849465.4 | 2058631.4 | 1901762.3
Long Term Average Sales | 2020474.4333 | 2020474.4333 | 2020474.4333 | 2020474.4333 | 2020474.4333 | 2020474.4333 | 2020474.4333 | 2020474.4333 | 2020474.4333 | 2020474.4333 | 2020474.4333 | 2020474.4333
Projection | 1631136.1 | 1700000 | 1700000
* Includes Exchange

## Slide 149: Regional Storage Reserves Could be Higher with California WaterFix
Chart: Million Acre-Feet
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Emergency Storage | 0.67 | 0.67 | 0.67 | 0.626 | 0.626 | 0.626 | 0.626 | 0.626 | 0.626 | 0.626
Dry-Year Storage | 2.2146 | 1.7816 | 1.064 | 0.99 | 1.672 | 2.368 | 2.739 | 2.324 | 1.2 | 0.87
Additional Storage with Cal Fix | 0 | 0 | 0.25585 | 0.45535 | 0.82635 | 0.87885 | 1.0293 | 1.3723 | 1.3944 | 1.4287
0.9
0.8
?
Storage represents end-of-year balances
1.43 million AF of
additional storage entering 2016
0.4
BiOps
Notes: From a local storage perspective, if we had the California WaterFix we could have an additional 1.43 million acre-feet of storage entering into 2016. Therefore, total MWD storage would be between 2.2 to 2.6 million acre-feet in 2016

## Slide 150: Design & Construction Enterprise Budget and Schedule

## Slide 151: California WaterFix Summary - Funding Commitments Mar 2016

## Slide 152: California WaterFix Summary - Funding Incurred Mar 2016

## Slide 153: Design & Construction Enterprise Annual & Cumulative Spending

## Slide 154
California WaterFix Program Budget Cumulative Cost (2014 Dollars) | 
Name | Cost
PM/CM/ENG | $ 1,919,910,670
Construction | $ 9,499,048,014
Contingency | $ 3,378,400,000
Land Acquisition | $ 146,100,000
Grand Total Cost | $ 14,943,458,684

## Slide 155
California WaterFix Mitigation Cost Estimate Cumulative Cost (2014 Dollars) |  |  | 
ID No. | Name | Cost | 
EC03 | Natural Communities Protection | $ 93,178,308 | 
EC04 | Tidal Natural Communities | $ 23,622,027 | 
EC06 | Channel Margin Enhancement | $ 39,654,662 | 
EC07 | Riparian Natural Community | $ 3,133,564 | 
EC08 | Grassland Restoration | $ 32,438,868 | 
EC09 | Vernal Pool and Alkali Seasonal Wetland | $ 75,000 | 
EC10 | Nontidal Marsh Restoration | $ 17,028,222 | 
EC11 | Natural Communities Management | $ 26,934,539 | 
EC15 | Localized Reduction of Predatory Fish | $ 19,703,298 | 
EC16 | Nonphysical Fish Barrier | $ 76,550,897 | 
CUL | Cultural Resources | $ 13,350,000 | 
AQ | Air Quality | $ 37,630,000 | 
BIO | Biological Resources | $ 12,000,000 | 
Subtotal |  | $ 395,299,385 | 
Other Costs |  |  | 
Program Administration |  |  | $ 12,775,000
Monitoring (terrestrial and aquatic) |  |  | $ 133,398,319
Property tax revenue replacement |  |  | $ 48,121,823
Subtotal |  |  | $ 194,295,142
Total Costs |  |  | $ 589,594,527
Contingency 35% |  |  | $ 206,358,084
Grand Total Cost |  |  | $ 795,952,611

## Slide 156
California WaterFix Total Budget Cumulative Cost (2014 Dollars) | 
Name | Cost
Total 2081/Section 7 Mitigation Costs | $ 795,952,611
Total Design/Construction Budget | $ 14,943,458,684
Grand Total Cost | $ 15,739,411,295

## Slide 157: Design and Construction Enterprise Organizational Structure
Program Director
Staffing and Admin.
Environment and Planning
Chief Engineer
QA / QC
General Technology
Environmental Permits
Tunnels & Shafts
Standards
Program Controls
Finance and Accounting
Public Education
Program Manager
Internal Audit
Legal Counsel
Program Director Reports
Program Manager Reports
Technical Leadership
Safety and Risk Mgmt.
Staffing
Office Management
Conveyance Mitigation Planning
Performance Management
Contracting
Utilities & Power
Program Controls and Contracting
Information Technology and Systems
Centralized Administration
Conveyance Mitigation Engineering
Intakes
Pumping Plant
Forebays
Geotech
Engineering Support
Estimating
Engineering Design Manager
Program Advisory Group
Property Acquisition
RoW, Survey & Mapping
Appraisal and Acquisitions
Work Team

## Slide 158
Start
Year 16
Pump Plant
2.25 Years
4.5 Years
7.25 Years
Clifton Court
7 Years
10.75 Years
4 Years
4 Years
3 Years
3 Years
3 Years
2.5 Years
2 Years
3 Years
1 Year
Commissioning
IF
Intake
Tunnel
Site Work
Utilities
IF
Clifton Court
Tunnel
Intake
Pump Plant
Utilities
RFQ process
Leadership staffing
.75 Years
1 Year
Design Phase
Construction Phase
Design and Construction Enterprise Program Schedule

## Slide 159
2016
Today
3099 days
12 Years
EC03 Natural Communities Protection
750 days
3 Years
EC04 Tidal Natural Communities
750 days
3 Years
EC06 Channel Margin Enhancement
1794 days
7 Years
EC07 Riparian Natural Community
2316 days
9 Years
EC08 Grassland Restoration
1534 days
6 Years
EC09 Vernal Pool and Alkali Seasonal Wetland
2315 days
9 Years
EC10 Non tidal Marsh Restoration
6751 days
26 Years
EC11 Natural Communities Management
6751 days
26 Years
EC15 Localized Reduction of Predatory Fish
6751 days
26 Years
EC16 Non physical Fish Barrier
Substantial Construction Completion
Start
Year 26
Design and Construction Enterprise Mitigation Program Schedule

## Slide 160: California WaterFix Draft Schedule Updated Dec 2015
2015
2017
TODAY
Jul
Oct
Jan
Apr
Jul
Oct
Jan
2016
59 days
23 days
190 days
115 days
81 days
95 days
70 days
32 days
20 days
56 days
11 days
21 days
5 days
34 days
196 days
23 days
67 days
44 days
45 days
229 days
EIR/S and ROD/NOD
SWRCB Permit
USACE 404 Permit
Biological Assessment and Opinion
Final BA
Apr 22
2016
BA Consultation and Response to Cmnts., ESA & CESA Negotiations
10/30/15
09/30/15
Draft BA/
2081(b)
Jul 10
2015
BiOp
4/29/16
Prepare Final EIR/EIS
ROD/
NOD
02/01/16
02/26/16
05/13/16
Lead
Agency
Review
Public Comments, Comment Response, Prepare Admin. Draft
Jun 20
2016
Jul 10
2015
Recirc. EIR/
EIS (NOA)
7/10/15
2081(b)
Permit App
11/13/15
2081(b) Permit
5/2/16
ROD/NOD*
6/20/16
Final EIR/EIS
5/13/16
SWRCB Petition
Public Notice of Petition, Hearing and Closing Briefs
Draft Order, and Comments on Draft Order
Consider Adoption
08/26/15
05/25/16
11/24/16
Jan 25
2017
Jul 10
2015
CPOD Approval—
Best Case
1/25/17
SWRCB Permit
Petition
8/26/15
Jun 21
2016
Aug 6
2015
404
Permit
App
9/24/15
401 Permit
Application
8/26/15
Section 106 Compliance
12/15/15
404 Permit
6/21/16

## Slide 161
2015
2017
Today
2016
59 days
23 days
190 days
115 days
81 days
95 days
70 days
32 days
20 days
56 days
11 days
21 days
5 days
34 days
196 days
23 days
67 days
44 days
45 days
229 days
EIR/S
SWRCB Permit
USACE 404 Permit
*BiOp is linked to the ROD/NOD | **Assumes no additional CEQA
Biological Assessment and Opinion
California WaterFix Draft Schedule: 2015-2017
Kern County Water Agency March 10, 2016
Final BA
Sep 6
2016
Section 7 Consultation
5/2/16
9/30/15
Draft BA/
2081(b)
Jul 10
2015
BiOp
9/6/16
Prepare
Final EIR/EIS
2/26/16
3/11/16
Lead
Agency
Review
Public Comments, Comment Response, Prepare Admin. Draft
May 13
2016
Jul 10
2015
Recirc. EIR/
EIS (NOA)
7/10/15
2081(b)
Permit App
4/15/16
2081(b) Permit
10/6/16
ROD/NOD*
9/16/16
Final EIR/EIS
5/13/16
Jan
Apr
Jul
Oct
2018
Jan
Apr
Jul
Oct
Jan
Apr
Jul
Oct
SWRCB Petition
Public Notice of Petition, Hearing and Closing Briefs
Draft Order, and Comments on Draft Order
Consider Adoption
8/26/15
Jul 10
2015
CPOD Approval**—
Most Likely
8/25/17
SWRCB Permit
Petition
8/26/15
1/26/17
6/26/17
Aug 25
2017
Dec 15
2016
Aug 6
2015
404
Permit
App
8/26/15
401 Permit
Application
9/24/15
Section 106 Compliance
4/29/16
404 Permit /
USACE ROD
4/25/17
404B1 Complete & USACE 404 Review
401 Certification
4/25/17

## Slide 162: California WaterFix Draft Schedule2016-2018
2016
2018
2017
2081(b)
Permit App
Final EIR/EIS
Jan
Apr
Section 106 Compliance
Jul
Oct
Jan
Apr
Jul
Oct
Jan
BiOp
2081(b) Permit
ROD/NOD*
404 Permit
404 Certification
Apr
Jul

## Slide 163: California WaterFix EIR/EIS Schedule 3-16-2016

## Slide 164: Delta Wetlands

## Slide 165: Regional Context
Bouldin Island
Bacon Island
Webb Tract
Holland Tract
Chipps Island

## Slide 166: General Location

## Slide 167: Bacon Island
Owner: Delta Wetlands Properties & Delta Wetlands Properties PTP
County: San Joaquin
5,603.17± acres
28 parcels
Land Use: Agricultural
Planted Acres: 4,860±

## Slide 168: Bouldin Island
Owner: Delta Wetlands Properties
County: San Joaquin
6,018.77± acres
35 parcels
Land Use: Agricultural
Planted Acres: 4,933±

## Slide 169: Holland Tract
Total Size:
  4,256.29± acres
  35 parcels
Owner: Delta Wetlands Properties (portion)
County: Contra Costa
3,007± acres
16 parcels
Land Use: Agricultural, Vacant, Recreational
Planted Acres: 3,020±

## Slide 170: Webb Tract
Owner: Delta Wetlands Properties
County: Contra Costa
5,497.86± acres
20 parcels
Land Use: Agricultural
Planted Acres: 4,064±

## Slide 171: Chipps Island
Owner: Delta Wetlands Properties
County: Solano
243± acres
1 parcel
Land Use: Agricultural

## Slide 172: Miscellaneous

## Slide 173: Metropolitan’s Average Annual Delta Diversions
Chart: Table A (in acre-ft.)
| 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Metropolitan Table A (AF) | 1057000 | 1157300 | 1257600 | 1358000 | 1458300 | 1558700 | 1659300 | 1759800 | 1860400 | 1961000 | 2011500 | 603450 | 905175 | 2011500 | 1005750 | 2011500 | 2011500 | 2011500 | 2011500 | 2011500 | 1810350 | 784485 | 1408050 | 1810350 | 1307475 | 1720350 | 1911500 | 1146900 | 669025 | 764600 | 955750 | 1529200 | 1242475 | 669025 | 95575 | 382300
Average diversions: 1980 – 2015 (1.39 maf), 1990 – 2015 (1.34 maf), 1980 – 2015 (1.14 maf)
1.39 million af average
Notes: Source: Governor’s Delta Vision Blue Ribbon Task Force Report Jan 2008, page 37; Measured, calculated and modeled data from an array of sources as compiled by Tully & Young, Inc. with data and assistance from DWR, the Bay Institute and the State Water Contractors.
Usage Trends Percent Acre-Feet (1990-2005)
Outflow to Ocean 48% 15,768,000 af
Upstream Consumptive Use 31% 10,183,500 af
CVP - SWP Exports 17% 5,584,500 af
In-Delta Consumptive Use 4% 1,314,000 af
TOTAL 100% 32,850,000 af
Southern Cal (Percent of Total 32.85 million AF)
MWD 3.7% 1,200,000 af
Bay Area (Percent of Total 32.85 million AF)
Contra Costa WD 0.35% 115,000 af
East Bay MUD 0.65% 213,000 af
San Francisco PUC 0.9% 302,000 af
Santa Clara Valley WD 1.3% 430,000 af
Alameda County 0.2% 56,000 af
TOTAL 3.4% 1,116,000 af
CCWD, EBMUD, SFPUC (Percent of Upstream Use 10.18 million AF)
Contra Costa WD 1.1% 115,000 af
East Bay MUD 2.1% 213,000 af
San Francisco PUC 3.0% 302,000 af
TOTAL 6.2% 630,000 af

## Slide 174: Southern California | Bay Area | In-Delta Users Each divert ~ 4% of the total annual runoff
Chart: 
| Outflow to Ocean | Upstream Consumptive Use | In-Delta Consumptive Use | MWD | CVP - SWP Exports
Usage Trends (1990 - 2005) | 0.48 | 0.31 | 0.04 | 0.05 | 0.12
Source: Governor’s Delta Vision Report (estimated total annual runoff 32.85 million acre-feet)
Bay area water agencies divert 3.5% of the total annual runoff
Pacific Ocean 48%
Upstream Consumptive Use 31%
Metropolitan Water District 4%
In-Delta Consumptive Use 4%
CVP-SWP Exports 17%
Notes: Source: Governor’s Delta Vision Blue Ribbon Task Force Report Jan 2008, page 37; Measured, calculated and modeled data from an array of sources as compiled by Tully & Young, Inc. with data and assistance from DWR, the Bay Institute and the State Water Contractors.
Usage Trends Percent Acre-Feet (1990-2005)
Outflow to Ocean 48% 15,768,000 af
Upstream Consumptive Use 31% 10,183,500 af
In-Delta Consumptive Use 4% 1,314,000 af
MWD (based on Table A) 5% 1,590,000 af
CVP - SWP Exports 12% 3,994,500 af
TOTAL 100% 32,850,000 af
Southern Cal (Percent of Total 32.85 million AF)
MWD (based on Table A) 4.8% 1,590,000 af
Bay Area (Percent of Total 32.85 million AF)
Contra Costa WD 0.35% 115,000 af
East Bay MUD 0.65% 213,000 af
San Francisco PUC 0.9% 302,000 af
Santa Clara Valley WD 1.3% 430,000 af
Alameda County 0.2% 56,000 af
TOTAL 3.4% 1,116,000 af
CCWD, EBMUD, SFPUC (Percent of Upstream Use 10.18 million AF)
Contra Costa WD 1.1% 115,000 af
East Bay MUD 2.1% 213,000 af
San Francisco PUC 3.0% 302,000 af
TOTAL 6.2% 630,000 af

## Slide 175: Governor’s Water Action Plan Supports ‘All of the Above’ Approach (Jan 2014)
Conservation
Regional self-reliance and integrated water management
Co-equal goals for the Delta
Protect and restore important ecosystems
Manage and prepare for dry periods
Water storage and groundwater management
Safe water for all communities
Flood protection
Operational and regulatory efficiency
Sustainable and integrated financing

## Slide 176: If the Delta is not Fixed, Billions of Dollars of Investments will be Stranded
State Water Project
  Construction
  Nearly 50 years of maintenance
Diamond Valley Lake
Inland Feeder
Water Treatment Processes

## Slide 177
Preliminary Subject to Revision
Tunnels
SJ River
Through Delta
CVP Pumps
SWP Pumps
Sacramento
Stockton
Sac River
West Canal
East Canal
Bay Delta Conservation Plan
Conveyance Alignment Options
177
Notes: 177
Here is the main website for information related to development of a long-term solution in the Delta (http://baydeltaconservationplan.com/Home.aspx). The BDCP Working Draft, dated November 18, 2010, is a good (but long) document detailing elements of the plan. Due to the size of the document, it can be downloaded from the following link (http://baydeltaconservationplan.com/BDCPPlanningProcess/DocumentsAndDrafts.aspx).

## Slide 178: California Treasurer’s Report & MWD’s Budget Forecast (in 2015 dollars)
Estimate in 2015 dollars
Metropolitan's 2013 estimate displayed in 2015 Dollars
Based on 20 hundred cubic feet per month
MWD sales of 1.7 million acre-feet and 50% reliance on MWD
Overall rate increase (including BDCP) ~ 3% to 5% per year
California Treasurer’s Report |  |  | MWD’s Budget & Rate Forecast Plan
Best Case | Base Case | Worst Case | 
$2 per month | $3 per month | $4 to 5 per month | $5/ month

## Slide 179: California WaterFix allows for improved capture of flood flows
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015
 | 451000 | 2531000 | 806000 | 474000 | 207000 | 200000
Wet
Below Normal
Dry
Critical
Storm Flow Period: | 1/20/10-3/16/10 | 12/7/10-7/11/11 | 1/23/12-5/16/12 | 12/1/12-2/17/13 | 2/9/14-4/10/14 | 12/12/14-1/11/15
Notes: Analysis by Metropolitan Water District of Southern California

## Slide 180: Staff Reference ONLY

## Slide 181: California WaterFix State Water Contractors Financing Agrmts

## Slide 182: California WaterFix State Water Project Agreements

## Slide 183
Labor costs include salary, leave and non-leave benefits
Other include charges for materials & supplies, trainings & seminars, conferences & meetings, and reprographics
MWD Expenditures on BDCP
Total (Jul 2005 – Sep 2015)
BDCP – Internal MWD Total Costs (~10 yrs.)
  Labor & Benefits (1) $ 20.91M
  Professional Services $ 4.15M
  Travel $ 1.03M
  Other (2) $ 0.14M
    Subtotal $ 26.23M
    Administrative Overhead $ 7.97M
    Total $ 34.20M
BDCP – Planning Cost by DWR
  BDCP/DHCCP $ 63M
As reported to Board on October 27, 2015
Notes: Labor
Based on staff estimates prior to 2011; Actual time from 2011 to present
Professional Services
Firms hired by MWD include – Dalldorf, Spezia, Beacon Economics, MWH, CDM, Cardno-Entrix, HNTB, AECOM, CH2MHill, Black & Veatch, URS, Geosyntech, ARUP, Anchor, Southern Cal Water Committee; Jacobs, Breakdown based on BDCP specific task orders through July 2015. Beginning FY 2015-16, all costs are tracked under PN 601118 although there are still some charges to old project numbers that were captured due to timing of invoice processing and adjustments for charges that were not previously reported.
Travel
Based on staff estimates prior to 2011; From 2011-2012, staff were charging to travel codes specific to BDCP; Starting in 2012, some staff began charging to a general Bay Delta code (PM07 – Travel, Incidentals, training, conferences, supplies, etc.), while others continued to charge to specific BDCP travel codes. Beginning in March 2015, staff started charging to specific projects to ensure that costs are properly reported.
Other
Others include charges for materials & supplies, trainings, seminars, conferences/meetings, & reprographics
Legal
Legal has a separate labor charge system; BDCP labor charges are not fully separated from other tasks; Labor calculated based on staff estimates of time spent on BDCP. Beginning in FY15-16, Legal has been reporting actual labor that are project specific.
FY2015-16 Cost Tracking
Tracking of BDCP expenditures have been consolidated under the same PN601118 beginning July 1, 2015. There are still some charges that were captured from the old project numbers mainly due to timing of data processing and reporting. These charges have since diminished and will hopefully end by the 2nd quarter for the fiscal year.

## Slide 184: Export Water Quality Improvements Salinity – BDCP Scenario 1
Chart: Avg Export Salinity (ppm)
| Pre-Court (D-1641) | Existing (Bio Op) | 3,000 cfs | 6,000 cfs | 9,000 cfs | 12,000 cfs | 15,000 cfs
Thru-Delta | 288 | 300
BDCP Ops 2010 (Scenario 1) | 264.8564 | 250.5841 | 241.241 | 234.6125 | 231.5898
Based on preliminary operations forwarded by BDCP Steering Comm in 2010 (Scenario 1)
Notes: Data from Armin Munevar & Chandra Chilmakuri (BDCP Steering Committee Presentation July 2010)
Pre-BO = 451 um/cm (289 mg/l)
Existing BO = 469 um/cm (300 mg/l)
Therefore, 4% degradation
Conversion from EC (um/cm) to TDS (mg/l or ppm) is 0.64; (TDS=0.64*EC)
Percent WQ improvement is based off of Existing BiOp
WQ Improvement (BDCP Scenario 1) – 3,000 cfs (12%), 6,000 cfs (16%), 9,000 cfs (20%), 12,000 cfs (22%), 15,000 cfs (23%)
Data from MWD Presentation
WQ “Above” Delta = 105 ppm TDS; 26 ppb TTHMs; 2 ppb Bromide; 2.2 ppm TOC
WQ “Export” = 300 ppm TDS; 99 ppb TTHMs; 314 ppb Bromide; 3.1 ppm TOC

## Slide 185: Delta Water Supply Analysis Alt. 1 – BDCP Steering Committee 2010 Proposal
Chart: Avg. SWP-CVP Exports (million AF)
| Pre-Court (D-1641) | Existing (BiOp-NAA) | 0 cfs | 3,000 cfs | 6,000 cfs | 9,000 cfs | 12,000 cfs | 15,000 cfs
South Delta Total | 5.9 | 4.7279 | 5.2762 | 4.4076 | 3.7663 | 3.3325 | 3.0878 | 2.9852
North Delta Total | 0 | 0 | 0 | 1.2553 | 2.0507 | 2.5602 | 2.8165 | 2.9283
Alt 1. BDCP Steering Committee Dec 2010 proposed operations
5.9
5.9
5.9
5.9
5.7
Metropolitan’s share ~ 25%

## Slide 186: Delta Water Supply Analysis Alt. 2 – Additional Fish Restrictions
Chart: Avg. SWP-CVP Exports (million AF)
| Pre-Court (D-1641) | Existing (BiOp-NAA) | 0 cfs | 3,000 cfs | 6,000 cfs | 9,000 cfs | 12,000 cfs | 15,000 cfs
South Delta Total | 5.9 | 4.7279 | 1.9227 | 1.8625 | 1.748 | 1.5552 | 1.3577 | 1.2447
North Delta Total | 0 | 0 | 0 | 1.6424 | 2.7266 | 3.3261 | 3.6714 | 3.8252
Alt 2. – Addtl Fish Restrictions analysis (Old & Middle River flows in Jan-May 0 cfs, Jun-Dec -2,000 cfs)
4.4
4.9
5.1
5.0
3.5
Metropolitan’s share ~ 25%

## Slide 187: Delta Water Supply Analysis Alt. 3 – Earthquake/No South Delta Diversion
Chart: Avg. SWP-CVP Exports (million AF)
| Pre-Court (D-1641) | Existing (BiOp-NAA) | 0 cfs | 3,000 cfs | 6,000 cfs | 9,000 cfs | 12,000 cfs | 15,000 cfs
South Delta Total | 5.9 | 4.7279 | 0 | 0 | 0 | 0 | 0 | 0
North Delta Total | 0 | 0 | 0 | 1.6183 | 2.8843 | 3.788 | 4.2996 | 4.4767
Alt 3. – Exports will be minimal for1.5 to 3 years following an earthquake
Metropolitan’s share ~ 25%

## Slide 188: New Conveyance Improvements Operations forwarded by Steering Comm (Yr. 2025)
Chart: Ave SWP-CVP Exports (AF)
| Pre-Court (D-1641) | Existing (Bio Op) | 3,000 cfs | 6,000 cfs | 9,000 cfs | 12,000 cfs | 15,000 cfs
Thru-Delta | 6.046 | 4.7 | 4.363 | 3.747 | 3.331 | 3.083 | 2.985
Isolated Facility | 0 | 0 | 1.327 | 2.09 | 2.568 | 2.82 | 2.928
South
Delta Exports
North
Delta Exports
Based on preliminary operations forwarded by BDCP Steering Comm in 2010

## Slide 189: Worsening Fishery Conditions More restrictive Old & Middle River conditions
Chart: Ave SWP-CVP Exports (AF)
| Pre-Court (D-1641) | No Fix (Bio Op) | 3,000 cfs | 6,000 cfs | 9,000 cfs | 12,000 cfs | 15,000 cfs
Thru-Delta | 6.046 | 3 | 1.897 | 1.787 | 1.595 | 1.391 | 1.28
Isolated Facility | 0 | 1.9 | 1.674 | 2.81 | 3.484 | 3.845 | 3.995
South
Delta Exports
North
Delta Exports
Based on preliminary operations forwarded by BDCP Steering Comm in 2010
Notes: BDCP assumed a scenario where OMR restrictions under more restrictive South Delta scenario:
Dec-Jun: OMR > 0 cfs
Jul-Nov: OMR > -2000 cfs

## Slide 190: No South Delta Diversions Due to sea-level rise, seismic/flood, ESA restrictions
Chart: Ave SWP-CVP Exports (AF)
| Pre-Court (D-1641) | No Fix (Bio Op) | 3,000 cfs | 6,000 cfs | 9,000 cfs | 12,000 cfs | 15,000 cfs
Thru-Delta | 6.046 | 4.9
Isolated Facility | 0 | 0 | 1.67 | 2.906 | 3.809 | 4.35 | 4.54
South
Delta Exports
North
Delta Exports
Based on preliminary operations forwarded by BDCP Steering Comm in 2010

## Slide 191
Goal – In-Delta Rivers Flowing Forward Old & Middle River Flows*
Chart: Old Middle River Flows (CFS)
| 0 cfs | 3,000 cfs | 6,000 cfs | 9,000 cfs | 12,000 cfs | 15,000 cfs
Existing BioOp | -1734.0133 | -1525.0324 | -1014.4348 | -288.1519 | 564.4207 | 1188.6313
More Restrictive south Delta
Fully isolated, no south Delta
* Average Old & Middle River flows January thru June
Larger tunnels eliminate reverse flows
Better Fish Flow Conditions
191
Notes: 191

## Slide 192: Biological Opinions for SWP/CVP Operations National Marine Fishery Service & US Fish & Wildlife Service

## Slide 194: Key Delta Operational Standards
Source | Action | Applicable Time Frame
D-1641 | Habitation Protection Flows between 7,100-29,200 cfs | February –June
D-1641 | Export/Inflow Ratio 35 % of Delta Inflow | February-June
D-1641 | San Joaquin River Inflow-to-Export Ratio of 1:1 | 31 days in April and May
D-1641 | Delta Cross Channel Gates Closed | February-May
D-1641 | Delta Cross Channel Gates conditionally closed | November - December
D-1641 | Minimum Delta Outflow | July - December
D-1641 | Minimum Sacramento River flow at Rio Vista | September - December
D-1641 | Minimum San Joaquin River flow at Vernalis | Additional releases up to 28 taf during Oct
D-1641 | 150 mg/l of chloride for Contra Costa Canal | Total of 150 days during a critically dry year
D-1641 | Southern Delta Electrical Conductivity | < 0.7 EC during April - August
D-1641 | Suisun Marsh Electrical Conductivity | October - May
NMFS BiOp Action IV.2.3 | OMR (-5000- -2500) until after June 1; Water Temperature at Mossdale less than or equal to 72 degrees for 7 days | January – mid May
NMFS BiOp Action IV.2.1 | SJR - Inflow/Export ratio | April 1—May 31
NMFS BiOp Action IV.1.2 | Delta Cross Channel Gates Conditionally closed | October - January
NMFS BiOp Action IV.1.2 | Delta Cross Channel Gates Closed | February - May
USFWS BiOp Action 1, 2, 3 | OMR Flow Restrictions & Turbidity Triggers(-1,250 to -5,000 cfs) | Dec - Jun
USFWS BiOp Action 5 | Install a barrier at the head of Old River | Spring

## Slide 195
Regulations (Existing & Proposed) | BDCP Preferred Alternative |  | NEW Cal WaterFix Preferred Alt.
 | Alt. 4-H3 | Alt. 4-H4 | Alt. 4A
Existing SWP/CVP Diversions (in 2015) |  |  | 
SWRCB D-1641 Regulations – Diversion Capacity | 6,000,000 af | 6,000,000 af | 6,000,000 af
2008 – Old & Middle River (USFWS BioOp) | - 700,000 af | - 700,000 af | - 700,000 af
2008 – Fall X2 Outflow (USFWS BioOp) | - 200,000 af | - 200,000 af | - 200,000 af
2009 – San Joaquin River I/E Ratio (NMFS) | - 300,000 af | - 300,000 af | - 300,000 af
SWP/CVP Diversions (in 2015) | 4,900,000 af | 4,900,000 af | 4,900,000 af
Proposed Fish Ops without North Intake (in 2025) |  |  | 
Existing SWP/CVP Diversions (in 2015) | 4,900,000 af | 4,900,000 af | 4,900,000 af
Potential – Climate Change Impacts by 2025 | - 200,000 af | - 200,000 af | - 200,000 af
Proposed – Enhanced Spring Outflow | - 0 af | - 600,000 af | - 300,000 af
Proposed – Add. OMR Restrictions (Scenario 6 ) | - 900,000 af | - 700,000 af | - 900,000 af
SWP/CVP Diversions without Fix (in 2025) | 3,800,000 af | 3,400,000 af | 3,500,000 af
Proposed Fish Ops with North Intake (in 2025) |  |  | 
SWP/CVP without North Intake (in 2025) | 3,800,000 af | 3,400,000 af | 3,500,000 af
Proposed – North Delta Restrictions | - 400,000 af | - 400,000 af | - 400,000 af
Proposed – North Delta Intake | + 1,900,000 af | + 1,700,000 af | + 1,800,000 af
SWP/CVP Diversions with Fix (in 2025) | 5,300,000 af | 4,700,000 af | 4,900,000 af
Proposed Fish Ops with North Intake & New Storage |  |  | 
North-of-Delta |  |  | 300,000 af
South-of-Delta |  |  | 200,000 af
SWP/CVP Diversions with Fix & Storage (in 2025) |  |  | 5,400,000 af
Delta Conveyance
Existing & Proposed SWP/CVP Diversion Regulations
Information produced by CH2M; Updated 11-25-2015
Rounding

## Slide 196
Regulations (Existing & Proposed) | BDCP Preferred Alternative |  | NEW Cal WaterFix Preferred Alt.
 | Alt. 4-H3 | Alt. 4-H4 | Alt. 4A
Existing SWP/CVP Diversions (in 2015) |  |  | 
SWRCB D-1641 Regulations – Diversion Capacity | 6,051,000 af | 6,051,000 af | 6,051,000 af
2008 – Old & Middle River (USFWS BioOp) | - 651,000 af | - 651,000 af | - 651,000 af
2008 – Fall X2 Outflow (USFWS BioOp) | - 183,000 af | - 183,000 af | - 183,000 af
2009 – San Joaquin River I/E Ratio (NMFS) | - 319,000 af | - 319,000 af | - 319,000 af
SWP/CVP Diversions (in 2015) | 4,898,000 af | 4,898,000 af | 4,898,000 af
Proposed Fish Ops without North Intake (in 2025) |  |  | 
Existing SWP/CVP Diversions (in 2015) | 4,898,000 af | 4,898,000 af | 4,898,000 af
Potential – Climate Change Impacts by 2025 | - 170,000 af | - 170,000 af | - 170,000 af
Proposed – Enhanced Spring Outflow | - 0 af | - 615,000 af | - 265,000 af
Proposed – Add. OMR Restrictions (Scenario 6 ) | - 914,000 af | - 667,000 af | - 914,000 af
SWP/CVP Diversions without Fix (in 2025) | 3,814,000 af | 3,446,000 af | 3,549,000 af
Proposed Fish Ops with North Intake (in 2025) |  |  | 
SWP/CVP without North Intake (in 2025) | 3,814,000 af | 3,446,000 af | 3,549,000 af
Proposed – North Delta Restrictions | - 419,000 af | - 419,000 af | - 419,000 af
Proposed – North Delta Intake | + 1,869,000 af | + 1,678,000 af | + 1,768,000 af
SWP/CVP Diversions with Fix (in 2025) | 5,265,000 af | 4,705,000 af | 4,898,000 af
Proposed Fish Ops with North Intake & New Storage |  |  | 
North-of-Delta |  |  | 292,000 af
South-of-Delta |  |  | 156,000 af
SWP/CVP Diversions with Fix & Storage (in 2025) |  |  | 5,346,000 af
Delta Conveyance
Existing & Proposed SWP/CVP Diversion Regulations
Information produced by CH2M; Updated 11-25-2015
No Rounding

## Slide 197
Month | Old & Middle River Criteria (Scenario 6) | BDCP Preferred Alternative |  | California WaterFix Preferred Alt.
 |  | Alt. 4-H3 | Alt. 4-H4 | Alt. 4A
Oct - Nov | No diversion during pulse flow -5,000 cfs in Nov | - 313,000 af | - 231,000 af | - 313,000 af
Dec - Mar | -5,000 to -3,000 cfs | -454,000 af | - 379,000 af | -454,000 af
Apr - May | -2,000 to +3,000 cfs | -60,000 af | - 51,000 af | -60,000 af
Jun | - 3,500 to + 1,000 cfs | -113,000 af | - 95,000 af | -113,000 af
Jul – Sep | No flow restrictions | +26,000 af | +89,000 af | +26,000 af
 | TOTAL Annual Impacts | - 914,000 af | - 667,000 af | - 914,000 af
Delta Conveyance
Additional Old & Middle River Reverse Flow Restrictions
Information produced by CH2M; Scenario 6 Breakdown

## Slide 198
Chart: Avg. SWP-CVP Export Capacity (MAF)
| 1980's | 1991 NMFS BioOp | 1992 CVPIA | 1994 Accord | 2000 Trinity River | 2006 San Joaquin River | 2008-09 Smelt/ Salmon BioOp | Future
SWP-CVP Exports | 8 | 7.9 | 6.7 | 6.2 | 5.6 | 5.4 | 4.7
9,000 cfs Facility
BDCP Enhanced Reliability
BDCP Replacement Supplies
SWP/CVP Export Capacity Restrictions Due to Environmental Regulations
State & Federal Project Supplies
History of Regulatory Restrictions
?

## Slide 199
Data based on hydrological period (1922-2003); indicates average annual SWP & CVP water supply exports with climate change in 2025
4.7 maf/yr – Existing Regulations (No Action Alternative) represents no new conveyance and no new/additional restrictions
3.5 maf/yr – BDCP Proposed Regulations without Northern Intake (Existing Conditions High Outflow Scenario); BDCP Chapter 9
1.5 maf/yr – Earthquake scenario BDCP Chapter 9; analyzed by Dr. David Sunding; minimal exports 1.5 to 3 years after earthquake
4.7 – 5.3 maf/yr – NEW BDCP / Cal Water Fix Preferred Alternative (evaluated in Draft EIR/S as Alternative 4A H3-H4)
4.7 – 5.6 maf/yr – PREVIOUS BDCP Preferred Alternative (evaluated in Draft EIR/S as Alternative 4 H1-H4 at early long-term 2025)
Chart: SWP-CVP Exports (million AF)
| Existing Regulations (No Action) | BDCP Regulations without North Intake | Earthquake Scenario | NEW BDCP/CA Water Fix Preferred (Alt. 4A H3-H4) | PREVIOUS BDCP Preferred (Alt. 4 H1-H4)
South Delta | 4.7 | 3.5 | 1.5 | 5.3 | 5.6
9,000 cfs Facility
State & Federal Project Supplies
Annual Average (in 2025)
Notes: 4.9 maf/yr – Current Supplies (2015)
4.7 maf/yr – Existing Regulations (No Action Alternative) represents no new conveyance and no new/additional restrictions
3.5 maf/yr – BDCP Proposed Regulations without Northern Intake represents the Existing Conditions High Outflow (ECHO) scenario without conveyance. Published in Chapter 9 (9.3.4.1.7 -- Practicability of the BDCP Proposed Action Relative to the Existing Conveyance High-Outflow and Low-Outflow Scenarios, pg. 9-45, 9-199, 9-207, 9-216, 9-224, 9-243, 9-250, and elsewhere). Also analyzed by Dr. Sunding.
1.5 maf/yr – Earthquake Scenario; Published in BDCP Chapter 9 -- the “mean water supplies following an earthquake in the Existing Conveyance High-Outflow Scenario are 1.0 MAF.” MWD is using a range from 1.0 to 1.5 maf
4.7 – 5.3 maf/yr – NEW BDCP / Cal Water Fix Preferred Alternative (evaluated in Draft EIR/S as Alternative 4A H3-H4 at early long-term 2025)
4.7 – 5.6 maf/yr – PREVIOUS BDCP Preferred Alternative (evaluated in Draft EIR/S as Alternative 4 H1-H4 at early long-term 2025)

## Slide 200
Chart: SWP-CVP Exports (million AF)
| Critical / Dry | Average | Wet
Existing Regulations / No Action (2025) | 3.6 | 4.7 | 5.8
9,000 cfs Facility
Cal Water Fix Alt 4a (2025) | 3.6 | 5.3 | 6.7
State & Federal Project Supplies
Existing Regulations vs. BDCP Cal Water Fix
SWP & CVP average annual water supply in 2025; Data from Recirculated Draft EIR/S
Existing Regulations
Cal Water Fix - Alt 4a
Notes: North and South Delta Exports for Alternative 4A –Dry and Critical Year Average (EIR/S Figure 4.3.1-17)
Existing Conditions = 4.1 maf
No Action (ELT in 2025) = 3.6 maf
Alt. H3 = 3.6 maf (2.6 maf South + 1.0 maf North)
Alt. H4 = 3.3 maf (2.4 maf South + 0.9 maf North)
North and South Delta Exports for Alternative 4A -Wet Year Average (EIS/R Figure 4.3.1-16)
Existing Conditions = 5.8 maf
No Action (ELT in 2025) = 3.6 maf
Alt. H3 = 6.7 maf (2.5 maf South + 4.2 maf North)
Alt. H4 = 6.0 maf (2.2 maf South + 3.8 maf North)
North and South Delta Exports for Alternative 4A –Long-Term Average (EIS/R Figure 4.3.1-15)
Existing Conditions = 5.1 maf
No Action (ELT in 2025) = 4.7 maf
Alt. H3 = 5.3 maf (2.7 maf South + 2.6 maf North)
Alt. H4 = 4.7 maf (2.4 maf South + 2.3 maf North)

## Slide 201
Chart: SWP-CVP Exports (million AF)
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033
Existing Regulations / No Action (2015-2020) | 4.9 | 4.9 | 4.88 | 4.86 | 4.84 | 4.82 | 4.8
Existing Regulations / No Action (2020 - 2030) | 3.6 | 3.575 | 3.55 | 3.5275 | 3.5 | 3.48 | 3.46 | 3.44 | 3.42 | 3.4 | 3.38
Cal Water Fix Alt 4a (2020 - 2030) | 4.8 | 4.7867 | 4.7733 | 4.76 | 4.7467 | 4.7333 | 4.72 | 4.7067 | 4.6933 | 4.68 | 4.63
Cal Water Fix Alt 4a (2020 - 2030)2 | 4.7 | 4.7 | 4.7
Cal Water Fix Alt 4a (2020 - 2030)3 | 5.3 | 5.3 | 5.3
State & Federal Project Supplies
Average Annual (million AF/yr)
SWP & CVP water supply analysis; Includes effect of climate change; Data from BDCP Draft EIR/S
4.9 – 4.6 maf/yr. – BDCP Record of Decision, collaborative adaptive management, with climate change
3.6 – 3.4 maf/yr. – BDCP proposed regulations without northern Intake (Existing Conditions High Outflow Scenario); BDCP Chapter 9
4.7 – 5.3maf/yr. – Cal Water Fix Alternative 4a, range of SWP/CVP supply improvements
No New Facilities Scenario
4.8 maf
3.6 maf
3.4 maf
4.9 maf
Existing
5.3 maf
4.7 maf
4.6 maf
Record of Decision Collaborative Adaptive Management
Cal Water Fix
Notes: MWD’s SWP Table A -- 45.81%
CVP/SWP Split
Using conveyance capacity -- CVP: 39%, SWP: 61%
Using contract amounts -- CVP south-of-Delta contractors: 28%, CVP (other): 17%, SWP: 55%
Total Water Supply -- CVP: 40.6%, SWP: 59.4%
Existing Condition (No Action) -- without BDCP conveyance approach
2015 – Exports = 4.9 maf (MWD= 1.23 maf)
2015-2020 – Exports ramp down from 4.9 to 4.8 maf (due to climate change)(MWD = 1.23 to 1.21)
2020 – Exports = 3.6 maf (new Bio Op with more restrictive OMR & more Spring outflow) (MWD = 0.91 maf)
2020-25 – Exports ramp down from 3.6 to 3.4 maf (due to climate change) (MWD = 0.86 maf)
BDCP Preferred Alternative 4A -- the with BDCP conveyance approach
2015 – Exports = 4.9 maf (MWD = 1.23 maf)
2015-2028 – Exports ramp down from 4.9 to 4.6 maf (due to climate change) (MWD = 1.23 to 1.18 maf)
2028 – Exports = 4.9 maf (Conveyance estimated online date) (MWD = 1.23 maf)
North and South Delta Exports for Alternative 4A –Long-Term Average (EIS/R Figure 4.3.1-15)
Existing Conditions = 5.1 maf
No Action (ELT in 2025) = 4.7 maf
Alt. H3 = 5.3 maf (2.7 maf South + 2.6 maf North)
Alt. H4 = 4.7 maf (2.4 maf South + 2.3 maf North)

## Slide 202: South Delta Reverse Flow Analysis California Water Fix Alt. 4a Elimination of Reserve Flow Enhances Fish Flow Conditions
Chart: Old Middle River Flows (CFS)
| 0 cfs | 3,000 cfs | 6,000 cfs | 9,000 cfs | 12,000 cfs | 15,000 cfs
Model Run | -1734.0133 | -1525.0324 | -1014.4348 | -229 | 564.4207 | 1188.6313
More Restrictive south Delta
Fully isolated, no south Delta
* Average Old & Middle River flows January thru June
Larger tunnels eliminate reverse flows
Better Fish Flow Conditions
202
Notes: 202

## Slide 204: Scaled Response Emergency Response Responsibilities in California

## Slide 205: USACE Capital & Operational Investments
Inventory Type | USACE (existing) | USACE(future)
Capital Budget |  | 
Warehouses/Storage Units | 1 multi-feature facility | 
Operations Budget |  | 
Hesco Barriers | 5,070 feet | 
Rapid Deploy Flood Wall | 1,920 feet | 
Port-a-Dam | 1,680 feet | 
Large Sandbags (3000 lb.) | 300 large bags | 
a Similar inventories on hand at 3 other USACE sites to augment stockpiles
Inventory Type | USACE (existing) | USACE(future)
Capital Budget |  | 
Warehouses/Storage Units | 1 multi-feature facility | 
Operations Budget |  | 
Hesco Barriers | 5,070 feet | a
Rapid Deploy Flood Wall | 1,920 feet | a
Port-a-Dam | 1,680 feet | a
Large Sandbags (3000 lb.) | 300 large bags | a

## Slide 206: DWR Capital Budget
Costs ($M) | FY 07/08 | FY 08/09 to Dec 14 | FY 14/15 | FY 15/16 | FY 16/17 | FY 17/18 | TOTAL ($M)
TOTAL (Proposition 1E) |  |  |  |  |  |  | $80.0
Loading & Storage Facilities |  | 1.2 | 4.2 | 12.4 | 7.6 |  | 25.4
Rock Stockpiles |  |  |  | 2.5 | 4.0 |  | 6.5
Sheet Pile Stockpiles |  | 0.2 | 0.2 | 2.5 | 5.8 |  | 8.7
Land Acquisition |  | 9.3 | 0.3 | 0.1 |  |  | 9.7
Emergency Response Predictive Model |  | 1.3 | 0.5 | 0.7 |  |  | 2.5
Agency Training & Emergency Exercises |  |  | 0.1 | 0.1 | 0.1 | 0.1 | 0.4
Delta Emergency Plan & Technical Studies |  | 5.3 | 0.5 | 0.2 |  |  | 6.0
Design & Administration |  | 5.2 | 1.9 | 2.4 | 0.9 | 0.4 | 10.8
Local Emergency Response Grants |  |  | 1.0 | 4.0 | 4.0 | 1.0 | 10.0
TOTAL (Proposition 84) |  |  |  |  |  |  | $13.9
Rock Stockpiles | 8.9 |  |  |  |  |  | 8.9
Communication Equipment |  | 5.0 |  |  |  |  | 5.0

## Slide 207: Seawater Desalination Permits

## Slide 208: Seawater Desalination Permits
Types of Regulations & Permits | 
Regulatory/Permit Activity | Responsible Fed/State Agency
Lease of coastal and/or offshore land | California State Lands Comm. (CSLC)
Coastal Development Permit | California Coastal Commission (CCC) Bay Conservation & Development Comm. (BCDC)
Environmental Impact Assessment/Report (EIA/EIR) | Local Coastal Program (LCP), CCC, BCDC and CSLC
Endangered Species Act | US Fish & Wildlife Service California Dept of Fish & Game
Marine Habitat Consultation | NOAA & National Marine Fisheries Service
Section 10 Rivers & Harbors Act Permit | Us Army Corps of Engineers
Section 316(b) of the Clean Water Act | State or Regional Water Quality Control Board CSLC
Section 401/404 of the Clean Water Act | US Army Corps of Engineers CSLC
Revised NPDES Permit | State or Regional Water Quality Control Board
Source: T. Secord, 2011 presentation

## Slide 209: Seawater Desalination Permitting Agencies
Effective & Comprehensive Permit Review
  Seawater desal facilities generally require the following State approvals:
  CEQA review: (sometimes by local gov’t)
  State Lands Commission: Tidelands Lease
  Coastal Commission: Coastal Permit
  State/Regional Water Boards: NPDES/Waste Discharge permit
  Public Health: Drinking water permit
Source: Coastal Commission Presentation, 2016

## Slide 210: Seawater Desalination Permitting: Process
Pre-application review
CEQA (and NEPA?)
Permitting – local, state, and federal
A final project!
Applicant
Other involved agencies
Local governments
Federal Agencies
State permitting agencies
Stakeholders
Source: Coastal Commission Presentation, 2016
Permit Review – much more than a State process!

## Slide 211: Seawater Desalination Permitting: Process
Source: Coastal Commission Presentation, 2016